## Slide 1: Bits, Bytes and Integers – Part 1 15-213/18-213/15-513: Introduction to Computer Systems 2nd Lecture, Aug. 31, 2017
Today’s Instructor:
Randy Bryant

## Slide 2: 数据的表示和运算(chapter2,课件2-4)
分三个部分介绍
  非数值数据的表示、数据的存储
    数据宽度单位
    硬件特征：大端/小端、对齐存放
  数值数据的表示
    定点数的编码表示
    整数的表示
    无符号整数、带符号整数
    浮点数的表示
    C语言程序的整数类型和浮点数类型

## Slide 3: 数据的表示和运算
分三个部分介绍（续）
  数据的运算
    按位运算和逻辑运算
    移位运算
    位扩展和位截断运算
    无符号和带符号整数的加减运算
    无符号和带符号整数的乘除运算
    变量与常数之间的乘除运算
从高级语言程序中的表达式出发，用机器数在具体电路中的执行过程，来解释表达式的执行结果
围绕C语言中的运算，解释其在底层机器级的实现方法

## Slide 4: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 5: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
15213: 0011 1011 0110 1101
3
B
6
D
Notes: C语言中表示16进制时，a-f大小写一致？

## Slide 6: Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 7: Machine Words
Any given computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 EB (exabytes) of addressable memory
    That’s 18.4 X 1018
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 8: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 9: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
pointer | 4 | 8 | 8
So, how are the bytes within a multi-byte word ordered in memory?
Notes: 字节
整形是32位

## Slide 10: 数据的存储和排列顺序
65535=216-1
[-65535]补=FFFF0001H
80年代开始，几乎所有机器都用字节编址
ISA设计时要考虑的两个问题：
  如何根据一个字节地址取到一个32位的字？- 字的存放问题
  一个字能否存放在任何字节边界？- 字的边界对齐问题
例如，若 int i = -65535，存放在内存100号单元（即占100#～103#），则用“取数”指令访问100号单元取出 i 时，必须清楚 i 的4个字节是如何存放的。
msb
lsb
103 102 101 100
little endian word 100#
100 101 102 103
big endian word 100#
Word:
FF FF 00 01
大端方式（Big Endian）: MSB所在的地址是数的地址
e.g. IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
小端方式（ Little Endian）: LSB所在的地址是数的地址
e.g. Intel 80x86, DEC VAX
有些机器两种方式都支持，可通过特定控制位来设定采用哪种方式。

## Slide 11: Representing Integers
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
IA32, x86-64
3B
6D
00
00
Sun
int A = 15213;
93
C4
FF
FF
IA32, x86-64
C4
93
FF
FF
Sun
Two’s complement representation
int B = -15213;
long int C = 15213;
00
00
00
00
6D
3B
00
00
x86-64
3B
6D
00
00
Sun
6D
3B
00
00
IA32
Increasing addresses

## Slide 12: BIG Endian versus Little Endian
Ex3: Memory layout of a instruction located in 1000
假定小端机器中指令：mov AX, 0x12345(BX)
其中操作码mov为40H，寄存器AX和BX的编号分别为0001B和0010B，立即数占32位，则存放顺序为：
若在大端机器上，则存放顺序如何？
40
1
2
00 01 23 45
40
1
2
45 23 01 00
00
01
23
45
12
40
45
23
01
00
12
40
1005
1004
1003
1002
1001
1000
地址
只需要考虑指令中立即数的顺序！

## Slide 13
Byte Swap Problem（字节交换问题）
78
56
34
12
0
1
2
3
increasing
byte
address
Big Endian
12
34
56
78
0
1
2
3
Little Endian
每个系统内部是一致的，但在系统间通信时可能会发生问题！
因为顺序不同，需要进行顺序转换
音、视频和图像等文件格式或处理程序都涉及到字节顺序问题
ex. Little endian: GIF, PC Paintbrush, Microsoft RTF,etc
Big endian: Adobe Photoshop, JPEG, MacPaint, etc
上述存放在0号单元的数据（字）是什么？
12345678H？ 78563412H？
存放方式不同的机器间程序移植或数据通信时，会发生什么问题？

## Slide 14: Alignment(对齐)
目前机器字长一般为32位或64位，而存储器地址按字节编址
指令系统支持对字节、半字、字及双字的运算，也有位处理指令
各种不同长度的数据存放时，有两种处理方式:
  按边界对齐 （假定存储字的宽度为32位，按字节编址）
    字地址：4的倍数(低两位为0)
    半字地址：2的倍数(低位为0)
    字节地址：任意
  不按边界对齐
    坏处：可能会增加访存次数！
Alignment: 要求数据的地址是相应的边界地址
每4个字节可同时读写

## Slide 15: Alignment(对齐)
按边界对齐
边界不对齐
0004081216
0 字节 1字节 2字节 3字节
0004081216
字节0 字节1 字节2 字节3
如：int i, short k, double x, char c, short j,……
则：&i=0; &k=4; &x=8; &c=16; &j=18;……
则： &i=0; &k=4; &x=6; &c=14; &j=15;……
x：3个周期
j：2个周期
x：2个周期
j：1个周期
虽节省了空间，但增加了访存次数！
需要权衡，目前来看，浪费一点存储空间没有关系！
存储器按字节编址
每次只能读写某个字地址开始的4个单元中连续的1个、2个、3个或4个字节

## Slide 16: Alignment(对齐) 举例
例如，考虑下列两个结构声明：
struct S1 {
int i；
char c；
int j；
}；
struct S2 {
int i；
int j；
char c；
}；
在要求对齐的情况下，哪种结构声明更好？
S1：
i
c
X X X
j
0
4
8
S2：
i
c
j
0
4
8
需要12个字节
只需要9个字节
对于“struct S2 d[4]”，只分配9个字节能否满足对齐要求？
S2：
i
c
X X X
j
0
4
8
不能！
也需要12个字节
S2比S1好
Notes: 2018.10.11

## Slide 17: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings
Notes: Manipulations：操作

## Slide 18
表示
  用一位表示 。例如，真：1 / 假：0
  N位二进制数可表示N个逻辑数据，或一个位串
运算
  按位进行
  如:按位与 / 按位或 / 逻辑左移 / 逻辑右移 等
识别
  逻辑数据和数值数据在形式上并无差别，也是一串0/1序列，机器靠指令来识别。
位串
  用来表示若干个状态位或控制位（OS中使用较多）
  例如，x86的标志寄存器含义如下：
逻辑数据的编码表示
CF
PF
AF
ZF
SF
TF
IF
DF
OF

## Slide 19: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both
Notes: Algebra: 代数

## Slide 20: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 → 0xBE
    ~010000012 → 101111102
  ~0x00 → 0xFF
    ~000000002 → 111111112
  0x69 & 0x55 → 0x41
    011010012 & 010101012 → 010000012
  0x69 | 0x55 → 0x7D
    011010012 | 010101012 → 011111012
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 21: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 → 0xBE
    ~010000012 → 101111102
  ~0x00 → 0xFF
    ~000000002 → 111111112
  0x69 & 0x55 → 0x41
    011010012 & 010101012 → 010000012
  0x69 | 0x55 → 0x7D
    011010012 | 010101012 → 011111012
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 → 0xBE
    ~0100 00012 → 1011 11102
  ~0x00 → 0xFF
    ~0000 00002 → 1111 11112
  0x69 & 0x55 → 0x41
    0110 10012 & 0101 01012 → 0100 00012
  0x69 | 0x55 → 0x7D
    0110 10012 | 0101 01012 → 0111 11012
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 22: Contrast: Logic Operations in C
Contrast to Bit-Level Operators
  Logic Operations: &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 → 0x00
  !0x00 → 0x01
  !!0x41→ 0x01
  0x69 && 0x55 → 0x01
  0x69 || 0x55 → 0x01
  p && *p (avoids null pointer access)
Watch out for && vs. & (and || vs. |)…
one of the more common oopsies in
C programming

## Slide 23: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000
Notes: Here

## Slide 24
特点
  是一种拼音文字，用有限几个字母可拼写出所有单词
  只对有限个字母和数学符号、标点符号等辅助字符编码
  所有字符总数不超过256个，使用7或8个二进位可表示
表示（常用编码为7位ASCII码）
  十进制数字：0/1/2…/9（30H）
  英文字母：A/B/…/Z/a/b/…/z（41H、61H）
  专用符号：+/-/%/*/&/……
  控制字符（不可打印或显示）（回车：0DH；换行：0AH）
操作
  字符串操作，如:传送/比较 等
西文字符的编码表示
必须熟悉对应的ASCII码！

## Slide 25: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings
Summary

## Slide 26: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign Bit
Notes: B2U:二进制到无符号数；B2T:二进制到真值
Complement: 补码

## Slide 27: Two-complement: Simple Example
10 =
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 0
-10 =
-16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0
8+2 = 10
-16+4+2 = -10

## Slide 28: Two-complement Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 29: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
  Minus 1
    111…1
Values for W = 16

## Slide 30: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 31: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 32: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 33: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret
Notes: T2B：真值（有符号数）到二进制；B2U：二进制到无符号数

## Slide 34: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 35: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux; int fun(unsigned u);
    uy = ty; uy = fun(tx);

## Slide 36: Casting Surprises
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
关系表达式 | 运算类型 | 结果 | 说明
0 == 0U -1 < 0 -1 < 0U 2147483647 > -2147483647-1 2147483647U > -2147483647-1 2147483647 > (int) 2147483648U -1 > -2 (unsigned) -1 > -2 |  |  | 

## Slide 37: C语言程序中的整数
关系 表达式 | 类 型 | 结 果 | 说明
0 = = 0U -1 < 0 -1 < 0U 2147483647 > -2147483647 - 1 2147483647U > -2147483647 - 1 2147483647 > (int) 2147483648U -1 > -2 (unsigned) -1 > -2 | 无 带 无 带 无 带 带 无 | 1 1 0* 1 0* 1* 1 1 | 00…0B = 00…0B 11…1B (-1) < 00…0B (0) 11…1B (232-1) > 00…0B(0) 011…1B (231-1) > 100…0B (-231) 011…1B (231-1) < 100…0B(231) 011…1B (231-1) > 100…0B (-231) 11…1B (-1) > 11…10B (-2) 11…1B (232-1) > 11…10B (232-2)
带*的结果与常规预想的相反！

## Slide 38: C语言程序中的整数
例如，考虑以下C代码：
1 int x = –1;
2 unsigned u = 2147483648;
3
4 printf ( “x = %u = %d\n”, x, x);
5 printf ( “u = %u = %d\n”, u, u);
在32位机器上运行上述代码时，它的输出结果是什么？为什么？
x = 4294967295 = –1
u = 2147483648 = –2147483648
因为–1的补码整数表示为“11…1”，作为32位无符号数解释时，其值为232–1= 4 294 967 296–1 = 4 294 967 295。
231的无符号数表示为“100…0”，被解释为32位带符号整数时，其值为最小负数：–232-1 = –231 = –2 147 483 648。

## Slide 39: C语言程序中的整数
1）在有些32位系统上，C表达式-2147483648 < 2147483647的执行结果为false。Why？
2）若定义变量“int i=-2147483648;”，则“i < 2147483647”的执行结果为true。Why？
3）如果将表达式写成“-2147483647-1 < 2147483647”，则结果会怎样呢？Why？
1）在ISO C90标准下 ，2147483648为unsigned类型，因此
“-2147483648 < 2147483647”按无符号数比较，
10……0B比01……1大，结果为false。
在ISO C99标准下 ，2147483648为int类型，因此
“-2147483648 < 2147483647”按带符号整数比较，
10……0B比01……1小，结果为true。
2）i < 2147483647 按int型数比较，结果为true。
3）-2147483647-1 < 2147483647 按int型比较，结果为true。

## Slide 40: Unsigned vs. Signed: Easy to Make Mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .

## Slide 41: Summary Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!

## Slide 42: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
  Summary
Representations in memory, pointers, strings

## Slide 43: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 44: Sign Extension: Simple Example
10 =
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 0
10 =
-32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 1 | 0 | 1 | 0
-10 =
-16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0
-32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 1 | 0
-10 =
Positive number
Negative number

## Slide 45: Larger Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 46: Truncation
Task:
  Given k+w-bit signed or unsigned integer X
  Convert it to w-bit integer X’ with same value for “small enough” X
Rule:
  Drop top k bits:
  X  = xw–1 , xw–2 ,…, x0
• • •
• • •
X 
w
X
• • •
• • •
w
k

## Slide 47: Truncation: Simple Example
10 =
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 0
-6 =
 | -8 | 4 | 2 | 1
 | 1 | 0 | 1 | 0
-10 =
-16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0
6 =
 | -8 | 4 | 2 | 1
 | 0 | 1 | 1 | 0
Sign change
2 =
-16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 0
2 =
 | -8 | 4 | 2 | 1
 | 0 | 0 | 1 | 0
-6 =
-16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 0
-6 =
 | -8 | 4 | 2 | 1
 | 1 | 0 | 1 | 0
No sign change
10 mod 16 = 10U mod 16 = 10U = -6
-10 mod 16 = 22U mod 16 = 6U = 6
2 mod 16 = 2
-6 mod 16 = 26U mod 16 = 10U = -6

## Slide 48: 举例
  例1（扩展操作）：在大端机上输出si, usi, i, ui的十进制和十六进制值是什么？
  short si = -32768;
  unsigned short usi = si;
  int i = si;
  unsingned ui = usi ;
si = -32768 80 00
usi = 32768 80 00
i = -32768 FF FF 80 00
ui = 32768 00 00 80 00
例2（截断操作）：i和j是否相等？
  int i = 32768;
  short si = (short) i;
  int j = si;
不相等！
i = 32768 00 00 80 00
si = -32768 80 00
j = -32768 FF FF 80 00
原因：对i截断时发生了“溢出”，即：32768截断为16位数时，因其超出16位能表示的最大值，故无法截断为正确的16位数！

## Slide 49: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small (in magnitude) numbers yields expected behavior

## Slide 50
小结
非数值数据的表示
  逻辑数据用来表示真/假或N位位串，按位运算
  西文字符：用ASCII码表示
  汉字编码
数据的宽度
  位、字节、字（不一定等于字长）
  k /K / M / G / T / P / E / Z / Y 有不同的含义
数据的存储排列
  数据的地址：连续若干单元中最小的地址，即：从小地址开始存放数据
    问题：若一个short型数据si存放在单元0x08000100和0x08000101中，那么si的地址是什么？
  大端方式：用MSB存放的地址表示数据的地址
  小端方式：用LSB存放的地址表示数据的地址
  按边界对齐可减少访存次数

## Slide 51
小结
在机器内部编码后的数称为机器数，其值称为真值
定义数值数据有三个要素：进制、定点/浮点、编码
整数的表示
  无符号数：正整数，用来表示地址等；带符号整数：用补码表示
C语言中的整数
  无符号数：unsigned int ( short / long)；带符号数： int ( short / long)
十进制数的表示：用ASCII码或BCD码表示
整形运算
  算术运算：无符号整数、有符号整数
  按位运算：“|”、“&”、“~”、“^”
  逻辑运算： “| |”、“& &”、“！”
  移位运算：“<<”、“>>”（逻辑移位、算术移位）
  位扩展和位截断：无符号和有符号