## Slide 1: Floating Point 15-213/18-213/15-513: Introduction to Computer Systems 4th Lecture, Sept. 7, 2017
Today’s Instructor:
Phil Gibbons

## Slide 2: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 3
Example:
mantissa (尾数) exponent(阶码、指数)
6.02 x 10 21
decimal point radix (base，基)
° Normalized form（规格化形式）: 小数点前只有一位非0数
° 同一个数有多种表示形式。例：对于数 1/1,000,000,000
• Normalized (唯一的规格化形式): 1.0 x 10-9
• Unnormalized（非规格化形式不唯一）: 0.1 x 10-8, 10.0 x 10-10
科学计数法(Scientific Notation)与浮点数
mantissa（尾数） exponent（指数）
0.101two x 2 -10
binary point 基为2
for Binary Numbers:
只要对尾数和指数分别编码，就可表示一个浮点数（即：实数）

## Slide 4: Fractional binary numbers
What is 1011.1012?

## Slide 5: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 6: Fractional Binary Numbers: Examples
Value Representation
5 3/4 = 23/4 101.112 = 4 + 1 + 1/2 + 1/4
2 7/8 = 23/8 010.1112 = 2 + 1/2 + 1/4 + 1/8
1 7/16 = 23/16 001.01112 = 1 + 1/4 + 1/8 + 1/16
Observations
  Divide by 2 by shifting right (unsigned)
  Multiply by 2 by shifting left
  Numbers of form 0.111111…2 are just below 1.0
    1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
    Use notation 1.0 – ε

## Slide 7: Representable Numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
    Limited range of numbers (very small values? very large?)
Notes: Rational numbers：有理数

## Slide 8
浮点数的表示
°Normal format（规格化数形式） ：
+/-1.xxxxxxxxxx × RExponent
°32-bit 规格化数：
31 0
S Exponent Significand
1 bit ? bits ? bits
S 是符号位（Sign）
Exponent用移码（增码）来表示
Significand 表示 xxxxxxxxxxxxx，尾数部分
(基可以是 2/ 4 / 8 / 16，约定信息，无需显式表示 )
°早期的计算机，各自定义自己的浮点数格式
问题：浮点数表示不统一会带来什么问题？

## Slide 9: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 10
“Father” of the IEEE 754 standard
现在所有计算机都采用IEEE 754来表示浮点数
1970年代后期, IEEE成立委员会着手制定浮点数标准
1985年完成浮点数标准IEEE 754的制定
Prof. William Kahan
www.cs.berkeley.edu/~wkahan/
ieee754status/754story.html
This standard was primarily the work of one person, UC Berkeley math professor William Kahan.
直到80年代初，各个机器内部的浮点数表示格式还没有统一
因而相互不兼容，机器之间传送数据时，带来麻烦

## Slide 11: IEEE Floating Point
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
  Some CPUs don’t implement IEEE 754 in full e.g., early GPUs, Cell BE processor
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard
Notes: 数字分析人员往往比硬件设计师更占据优势
Rounding：舍入

## Slide 12: Floating Point Representation
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac
  Example: 1521310 = (-1)0 x 1.11011011011012 x 213

## Slide 13: Precision options
Single precision: 32 bits  7 decimal digits, 10±38
Double precision: 64 bits  16 decimal digits, 10±308
Other formats: half precision, quad precision
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits

## Slide 14: Three “kinds” of floating point numbers
s | exp | frac
1 | e-bits | f-bits
00…00
exp ≠ 0 and exp ≠ 11…11
11…11
denormalized
normalized
special

## Slide 15: “Normalized” Values
When: exp ≠ 000…0 and exp ≠ 111…1
Exponent coded as a biased value: E = exp – Bias
  exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (exp: 1…254, E: -126…127)
    Double precision: 1023 (exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free”
v = (–1)s M 2E
Notes: Bias：[ˈbaɪəs]

## Slide 16: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = exp – Bias
Notes: Significand：尾数

## Slide 17
IEEE 754标准
Single Precision ：
S Exponent Significand
1 bit 8 bits 23 bits
° Sign bit: 1 表示negative ; 0表示 positive
°Significand（尾数）:
• 规格化尾数最高位总是1，所以隐含表示，省1位
• 1 + 23 bits （ single），1 + 52 bits （double）
°Exponent（阶码 / 指数）:
    SP规格化数阶码范围为0000 0001 (-126) ~ 1111 1110 (127)
    bias为127 (single), 1023 (double)
SP: (-1)S x (1 + Significand) x 2(Exponent-127)
DP: (-1)S x (1 + Significand) x 2(Exponent-1023)
全0和全1用来表示特殊值！
  为什么用127？若用128,则阶码范围为多少？
  0000 0001 (-127) ～ 1111 1110 (126)
规格化数：+/-1.xxxxxxxxxxtwo x 2Exponent
规定：小数点前总是“1”，故可隐含表示。注意：和前面例子规定不一样,这里更合理!

## Slide 18: Ex: Converting Binary FP to Decimal
1011 11101 110 0000 0000 0000 0000 0000
°Sign: 1 => negative
°Exponent:
• 0111 1101two = 125ten
• Bias adjustment: 125 - 127 = -2
°Significand:
1 + 1x2-1+ 1x2-2 + 0x2-3 + 0x2-4 + 0x2-5 +...
=1+2-1 +2-2 = 1+0.5 +0.25 = 1.75
°Represents: -1.75tenx2-2 = - 0.4375
(-1)S x (1 + Significand) x 2(Exponent-127)
BEE00000H is the hex. Rep. Of an IEEE 754 SP FP number
Notes: If we know the hexadecimal representation of an IEEE 754 single precision number, how to calculate the actual value of this number? Here is an example. Suppose the hex form is BEE00000H. At first, we should convert the hex form to binary form, we get the binary form 1011 1110 1110 0000 0000 …0000, and for single precision, we have 1 sign bit, which is 1, 8 bits for exponent, which is 0111 11101, and the remainder is 23-bit significand. Then we can use the formula to calculate the value.
Step 1: sign bit is 1, it means the number is negative
Step 2: exponent is 01111101=26 +25 + 24 +23 +21 =64+32+16+8+1=125, because we use excess 127, so we should subtract 127 to get the actual value of exponent. 125-127=-2
Step 3: here actual mantissa is 1.1100..0, so the value should be 1+…., …. The result is 1.75
Step 4: So the actual value is
Any question about that?

## Slide 19: Ex: Converting Decimal to FP
-12.75
1. Denormalize: -12.75
2. Convert integer part:
12 = 8 + 4 = 11002
3. Convert fractional part:
.75 = .5 + .25 = .112
4. Put parts together and normalize:
1100.11 = 1.10011 x 23
5. Convert exponent: 127 + 3 = 128 + 2 = 1000 00102
11000 0010 100 1100 0000 0000 0000 0000
The Hex rep. is C14C0000H
Notes: If we know the value of an number, how to represent it in floating-point form? Here is an exercise. Please spend 4 minutes to try it.
Let’s check your answers. Firstly, then, and then, finally, the result is C14C0000H. Have you got that? Any question?

## Slide 20: Normalized numbers（规格化数）
Exponent Significand Object
1-254 anything Norms
implicit leading 1
0 0 ?
0 nonzero ?
255 0 ?
255 nonzero ?
前面的定义都是针对规格化数（normalized form）
How about other patterns?

## Slide 21: Denormalized Values
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of exp – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (表示不同含义)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced（可能的数值分布均匀地接近0）
v = (–1)s M 2E
E = 1 – Bias
Notes: 规格化数不能表示0，只有M=0时为+0和-0.

## Slide 22: Special Values
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 23: Visualization: Floating Point Encodings
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 24: C float Decoding Example
float: 0xC0A00000
binary:
1 | 8-bits | 23-bits
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
  Bias = 2k-1 – 1 = 127

## Slide 25: C float Decoding Example
E = 129
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E =
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits

## Slide 26: C float Decoding Example
float: 0xC0A00000
binary: 1100 0000 1010 0000 0000 0000 0000 0000
1 | 1000 0001 | 010 0000 0000 0000 0000 0000
1 | 8-bits | 23-bits
E = exp – Bias = 129 – 127 = 2 (decimal)
S = 1 -> negative number
M = 1.010 0000 0000 0000 0000 0000
M = 1 + 1/4 = 1.25
v = (–1)s M 2E
E = exp – Bias
v = (–1)s M 2E = (-1)1 * 1.25 * 22 = -5
  Bias = 2k-1 – 1 = 127

## Slide 27: Today: Floating Point
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Rounding, addition, multiplication
Floating point in C
Summary

## Slide 28: Floating Point in C
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode
Notes: Int到float会舍入，位数相同，float到int会舍弃小数部分

## Slide 29: Floating Point Puzzles
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN

## Slide 30: C语言中的浮点数类型-32位
C语言中有float和double类型，分别对应IEEE 754单精度浮点数格式和双精度浮点数格式
long double类型的长度和格式随编译器和处理器类型的不同而有所不同，IA-32中是80位扩展精度格式
从int转换为float时，不会发生溢出，但可能有数据被舍入
从int或 float转换为double时，因为double的有效位数更多，故能保留精确值
从double转换为float和int时，可能发生溢出，此外，由于有效位数变少，故可能被舍入
从float 或double转换为int时，因为int没有小数部分，所以数据可能会向0方向被截断

## Slide 31: Summary
IEEE Floating Point has clear mathematical properties
Represents numbers of form M x 2E
One can reason about operations independent of implementation
  As if computed with perfect precision and then rounded
Not the same as real arithmetic
  Violates associativity/distributivity
  Makes life difficult for compilers & serious numerical applications programmers