## Slide 1: Machine-Level Programming I: Basics 15-213/18-213/15-213: Introduction to Computer Systems 5th Lecture, September 12, 2017
Today’s Instructor:
Phil Gibbons

## Slide 2
程序的转换与机器级表示
主要教学目标
  了解高级语言与汇编语言、汇编语言与机器语言之间的关系
  掌握有关指令格式、操作数类型、寻址方式、操作类型等内容
  了解高级语言源程序中的语句与机器级代码之间的对应关系
  了解复杂数据类型（数组、结构等）的机器级实现
主要教学内容
  介绍C语言程序与机器级指令之间的对应关系。
  主要包括：程序转换概述、IA-64指令系统、C语言中控制语句和过程调用等机器级实现、复杂数据类型（数组、结构等）的机器级实现等。
  本章所用的机器级表示主要以汇编语言形式表示为主。
采用逆向工程方法！

## Slide 3
程序的机器级表示
分以下五个部分介绍
  第一讲：程序转换概述
    机器指令和汇编指令
    机器级程序员感觉到的属性和功能特性
    高级语言程序转换为机器代码的过程
  第二讲：IA-32 /x86-64指令系统
  第三讲： C语言程序的机器级表示
    选择语句的机器级表示
    循环结构的机器级表示
    过程调用的机器级表示
  第四讲：复杂数据类型的分配和访问
    数组的分配和访问
    结构体数据的分配和访问
    联合体数据的分配和访问
    数据的对齐
  第五讲：越界访问和缓冲区溢出
从高级语言程序出发，用其对应的机器级代码以及内存（栈）中信息的变化来说明底层实现
围绕C语言中的语句和复杂数据类型，解释其在底层机器级的实现方法

## Slide 4
“指令”的概念
计算机中的指令有微指令、机器指令和伪（宏）指令之分
微指令是微程序级命令，属于硬件范畴
伪指令是由若干机器指令组成的指令序列，属于软件范畴
机器指令介于二者之间，处于硬件和软件的交界面
  本章中提及的指令都指机器指令
汇编指令是机器指令的汇编表示形式，即符号表示
机器指令和汇编指令一一对应，它们都与具体机器结构有关，都属于机器级指令

## Slide 5
机器级指令
机器指令和汇编指令一一对应，都是机器级指令
机器指令是一个0/1序列，由若干字段组成
汇编指令是机器指令的符号表示（可能有不同的格式）
  mov、movb、bx、%bx等都是助记符
  指令的功能为：M[R[bx]+R[di]-6]←R[cl]
操作码 寻址方式 寄存器编号 立即数(位移量)
mov [bx+di-6], cl
movb %cl, -6(%bx,%di)
或
Intel格式
AT&T 格式
补码11111010的真值为多少？
寄存器传送语言 RLT（Register Transfer Language）
R：寄存器内容
M：存储单元内容

## Slide 6
计算机中数据的存储
计算机中的数据存放在哪里？
寄存器文件
通用寄存器组GPRs
存储器
指令中需给出的信息：
操作性质（操作码）
源操作数1 或/和 源操作数2 （立即数、寄存器编号、存储地址）
目的操作数地址 （寄存器编号、存储地址）
存储地址的描述与操作数的数据结构有关！

## Slide 7
I/O
CPU
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
MM
Assembler
指令集体系结构ISA
ISA（Instruction Set Architecture）位于软件和硬件之间
硬件的功能通过ISA提供出来
软件通过ISA规定的”指令”使用硬件
ISA规定了：
  可执行的指令的集合，包括指令格式、操作种类以及每种操作对应的操作数的相应规定；
  指令可以接受的操作数的类型；
  操作数所能存放的寄存器组的结构，包括每个寄存器的名称、编号、长度和用途；
  操作数所能存放的存储空间的大小和编址方式；
  操作数在存储空间存放时按照大端还是小端方式存放；
  指令获取操作数的方式，即寻址方式；
  指令执行过程的控制方式，包括程序计数器、条件码定义等。

## Slide 8: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 9: Levels of Abstraction
C programmer
Assembly programmer
Computer Designer
C code
Caches, clock freq, layout, …
Nice clean layers, but beware…
Of course, you know that: It’s why you are taking this course.

## Slide 10: Definitions
Architecture: (also ISA: instruction set architecture) The parts of a processor design that one needs to understand for writing correct machine/assembly code
  Examples: instruction set specification, registers
  Machine Code: The byte-level programs that a processor executes
  Assembly Code: A text representation of machine code
Microarchitecture: Implementation of the architecture
  Examples: cache sizes and core frequency
Example ISAs:
  Intel: x86, IA32, Itanium, x86-64
  ARM: Used in almost all mobile phones
  RISC V: New open-source ISA

## Slide 11: Assembly/Machine Code View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic or logical operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte addressable array
    Code and user data
    Stack to support procedures

## Slide 12: Assembly Characteristics: Data Types
“Integer” data of 1, 2, 4, or 8 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
(SIMD vector data types of 8, 16, 32 or 64 bytes)
Code: Byte sequences encoding series of instructions
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 13: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
  Not part of memory (or cache)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 14: Some History: IA32 Registers
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)
Notes: %al,%ah,%ax,%eax,%rax这些寄存器可以直接使用
Obsolete-废弃的；老式的

## Slide 15: Assembly Characteristics: Operations
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Perform arithmetic function on register or memory data
Transfer control
  Unconditional jumps to/from procedures
  Conditional branches
  Indirect branches

## Slide 16
IA-32的寻址方式
寻址方式
  根据指令给定信息得到操作数或操作数地址
操作数所在的位置
  指令中：立即寻址
  寄存器中：寄存器寻址
  存储单元中（属于存储器操作数，按字节编址）：其他寻址方式
存储器操作数的寻址方式与微处理器的工作模式有关
  两种工作模式：实地址模式和保护模式
实地址模式（基本用不到）
  为与8086/8088兼容而设，加电或复位时
  寻址空间为1MB，20位地址：(CS)<<4+(IP)
保护模式（需要掌握）
  加电后进入，采用虚拟存储管理，多任务情况下隔离、保护
  80286以上高档微处理器最常用的工作模式
  寻址空间为232B，32位线性地址分段（段基址+段内偏移量）

## Slide 17
保护模式下的寻址方式
SR段寄存器（间接）确定操作数所在段的段基址
有效地址给出操作数在所在段的偏移地址
存储器操作数
跳转目标指令地址

## Slide 18
存储器操作数的寻址方式(32位)
int x；
float a[100];
short b[4][4];
char c;
long *c1;
double d[10];
a[i]的地址如何计算？
104+i×4
i=99时，104+99×4=500
b[i][j]的地址如何计算？
504+i×8+j×2
i=3、j=2时，504+24+4=532
d[i]的地址如何计算？
544+i×8
i=9时，544+9×8=616
b31 b0
x
a[0]
a[99]
b[0][1]
100
104
b[0][0]
b[3][3]
b[3][2]
c
500
504
532
536
544
d[0]
d[9]
616
对齐

## Slide 19
存储器操作数的寻址方式
各变量应采用什么寻址方式？
x、c：位移 / 基址
a[i]：104+i×4，比例变址+位移
d[i]：544+i×8，比例变址+位移
b[i][j]： 504+i×8+j×2，
基址+比例变址+位移
int x；
float a[100];
short b[4][4];
char c;
long *c1;
double d[10];
b31 b0
x
a[0]
a[99]
b[0][1]
100
104
b[0][0]
b[3][3]
b[3][2]
c
500
504
532
536
544
d[0]
d[9]
616
将b[i][j]取到EAX中的指令可以是：
“movw 504(%ebp,%esi,2), %eax”
其中， i×8在EBP中，j在ESI中，
2为比例因子

## Slide 20: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “addressing modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rn(n=8~15)
Warning: Intel docs use mov Dest, Source
ATT格式
C，C++规定，16进制数必须以 0x开头

## Slide 21: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest

## Slide 22: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx
Notes: （）：表示间接寻址
Pointer dereferencing：指针的间接引用

## Slide 23: Example of Simple Addressing Modes
whatAmI:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
void
whatAmI(<type> a, <type> b)
{
????
}
%rdi
%rsi

## Slide 24: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 25: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 26: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 27: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 28: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 29: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 30: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address

## Slide 31: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 32: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 16 integer registers
  Ri: Index register: Any, except for %rsp
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 33: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100
Notes: 0xf000 + 0x8 = 0xf008
0xf000 + 0x0100 = 0xf100
0xf000 + 4*0x0100 = 0xf400
2*0xf000 + 0x80 = 0x1d080

## Slide 34: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 35
IA-32常用指令类型
（1）传送指令
  通用数据传送指令
    MOV：一般传送，包括movb、movw和movl等
    MOVS：符号扩展传送，如movsbw、movswl等
    MOVZ：零扩展传送，如movzwl、movzbl等
    XCHG：数据交换
    PUSH/POP：入栈/出栈，如pushl,pushw,popl,popw等
  地址传送指令
    LEA：加载有效地址，如leal (%edx,%eax), %eax”的功能为R[eax]←R[edx]+R[eax]，执行前，若R[edx]=i，R[eax]=j，则指令执行后，R[eax]=i+j
  输入输出指令
    IN和OUT：I/O端口与寄存器之间的交换
  标志传送指令
    PUSHF、POPF：将EFLAG压栈，或将栈顶内容送EFLAG

## Slide 36
IA-32常用指令类型
（2）定点算术运算指令
  加 / 减运算（影响标志、不区分无/带符号）
    ADD：加，包括addb、addw、addl等
    SUB：减，包括subb、subw、subl等
  增1 / 减1运算（影响除CF以外的标志、不区分无/带符号）
    INC：加，包括incb、incw、incl等
    DEC：减，包括decb、decw、decl等
  取负运算（影响标志、若对0取负，则结果为0/CF=0,否则CF=1）
    NEG：取负，包括negb、negw、negl等
  比较运算（做减法得到标志、不区分无/带符号）
    CMP：比较，包括cmpb、cmpw、cmpl等
  乘 / 除运算（不影响标志、区分无/带符号）
    MUL / IMUL：无符号乘 / 带符号乘
    DIV/ IDIV：带无符号除 / 带符号除

## Slide 37
IA-32常用指令类型
（3）按位运算指令
  逻辑运算（仅NOT不影响标志，其他指令OF=CF=0，而ZF和SF根据结果设置：若全0，则ZF=1；若最高位为1，则SF=1 ）
    NOT：非，包括 notb、notw、notl等
    AND：与，包括 andb、andw、andl等
    OR：或，包括 orb、orw、orl等
    XOR：异或，包括 xorb、xorw、xorl等
    TEST：做“与”操作测试，仅影响标志
  移位运算（左/右移时，最高/最低位送CF）
    SHL/SHR：逻辑左/右移，包括 shlb、shrw、shrl等
    SAL/SAR：算术左/右移，左移判溢出，右移高位补符
    ROL/ROR: 循环左/右移，包括 rolb、rorw、roll等
    RCL/RCR: 带循环左/右移，将CF作为操作数一部分循环移位
以上内容不要死记硬背，遇到具体指令时能查阅到并理解即可。

## Slide 38
IA-32常用指令类型
（4）控制转移指令
指令执行可按顺序 或 跳转到转移目标指令处执行
  无条件转移指令
    JMP DST：无条件转移到目标指令DST处执行
  条件转移
    Jcc DST：cc为条件码，根据标志（条件码）判断是否满足条件，若满足，则转移到目标指令DST处执行，否则按顺序执行
  条件设置
    SETcc DST：将条件码cc保存到DST（通常是一个8位寄存器 ）
  调用和返回指令 （用于过程调用）
    CALL DST：返回地址RA入栈，转DST处执行
    RET：从栈中取出返回地址RA，转到RA处执行
以上内容不要死记硬背，遇到具体指令时能查阅到并理解即可。

## Slide 39: Address Computation Instruction
leaq Src, Dst
  Src is address mode expression
  Set Dst to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t = x+2*x
salq $2, %rax # return t<<2
Converted to ASM by compiler:
leaq ($0x1000), %rax # %rax = 1000H
leaq (%rbx), %rax # %rax = %rbx
Notes: Lea-load effective address
Computing addresses without a memory reference-计算地址，但没有引用内存

## Slide 40: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src Also called shlq
    sarq Src,Dest Dest = Dest >> Src Arithmetic
    shrq Src,Dest Dest = Dest >> Src Logical
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order! Src,Dest (Warning: Intel docs use “op Dest,Src”)
No distinction between signed and unsigned int (why?)

## Slide 41: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions

## Slide 42: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret
Notes: 解释c语言代码和汇编语言对应关系，汇编语言：1、rax=x+y；2、rax=x+y+z；3、rdx=3y；4、rdx=48y；5、rcx=x+48y+4；6、rax=rcx*rax

## Slide 43: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z, t4
%rax | t1, t2, rval
%rcx | t5

## Slide 44: Today: Machine Programming I: Basics
History of Intel processors and architectures
Assembly Basics: Registers, operands, move
Arithmetic & logical operations
C, assembly, machine code

## Slide 45: Turning C into Object Code
text
text
binary
binary
Compiler (gcc –Og -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc –Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of GCC]
    Put resulting binary in file p

## Slide 46: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on shark machine) with command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on non-Shark machines (Andrew Linux, Mac OS-X, …) due to different versions of gcc and different compiler settings.

## Slide 47: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore

## Slide 48: What it really looks like
.globl sumstore
.type sumstore, @function
sumstore:
.LFB35:
.cfi_startproc
pushq %rbx
.cfi_def_cfa_offset 16
.cfi_offset 3, -16
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
.cfi_def_cfa_offset 8
ret
.cfi_endproc
.LFE35:
.size sumstore, .-sumstore
Things that look weird and are preceded by a ‘.’ are generally directives.
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret

## Slide 49
GCC使用举例
两个源程序文件test1.c和test2.c，最终生成可执行文件为test
  gcc -O1 test1.c test2.c -o test
选项-O1表示一级优化，-O2为二级优化，选项-o指出输出文件名
目标文件可用“objdump -d test.o” 反汇编为汇编语言程序
add:
pushl %ebp
movl %esp, %ebp
subl $16, %esp
movl 12(%ebp), %eax
movl 8(%ebp), %edx
leal (%edx, %eax), %eax
movl %eax, -4(%ebp)
movl -4(%ebp), %eax
leave
ret
00000000 <add>:
0: 55 push %ebp
1: 89 e5 mov %esp, %ebp
3: 83 ec 10 sub $0x10, %esp
6: 8b 45 0c mov 0xc(%ebp), %eax
9: 8b 55 08 mov 0x8(%ebp), %edx
c: 8d 04 02 lea (%edx,%eax,1), %eax
f: 89 45 fc mov %eax, -0x4(%ebp)
12: 8b 45 fc mov -0x4(%ebp), %eax
15: c9 leave
16: c3 ret
gcc -E test.c -o test.i
gcc -S test.i -o test.s
gcc –S test.c –o test.s
test.s
位移量
机器指令
汇编指令
编译得到的与反汇编得到的汇编指令形式稍有差异

## Slide 50
两种目标文件
“objdump -d test” 结果
00000000 <add>:
0: 55 push %ebp
1: 89 e5 mov %esp, %ebp
3: 83 ec 10 sub $0x10, %esp
6: 8b 45 0c mov 0xc(%ebp), %eax
9: 8b 55 08 mov 0x8(%ebp), %edx
c: 8d 04 02 lea (%edx,%eax,1), %eax
f: 89 45 fc mov %eax, -0x4(%ebp)
12: 8b 45 fc mov -0x4(%ebp), %eax
15: c9 leave
16: c3 ret
test.o中的代码从地址0开始，test中的代码从80483d4开始！
080483d4 <add>:
80483d4: 55 push ...
80483d5: 89 e5 …
80483d7: 83 ec 10 …
80483da: 8b 45 0c …
80483dd: 8b 55 08 …
80483e0: 8d 04 02 …
80483e3: 89 45 fc …
80483e6: 8b 45 fc …
80483e9: c9 …
80483ea: c3 ret
“objdump -d test.o”结果
test.o：可重定位目标文件
test：可执行目标文件

## Slide 51: Object Code
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 14 bytes
  Each instruction 1, 3, or 5 bytes
  Starts at address 0x0400595

## Slide 52: Machine Instruction Example
C Code
  Store value t where designated by dest
Assembly
  Move 8-byte value to memory
    Quad words in x86-64 parlance
  Operands:
    t: Register %rax
    dest: Register %rbx
    *dest: Memory M[%rbx]
Object Code
  3-byte instruction
  Stored at address 0x40059e
*dest = t;
movq %rax, (%rbx)
0x40059e: 48 89 03

## Slide 53: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 54: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore

## Slide 55: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  Disassemble procedure
  gdb sum
  disassemble sumstore
  Examine the 14 bytes starting at sumstore
  x/14xb sumstore
Object Code
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 56: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 57: Machine Programming I: Summary
History of Intel processors and architectures
  Evolutionary design leads to many quirks and artifacts
C, assembly, machine code
  New forms of visible state: program counter, registers, ...
  Compiler must transform statements, expressions, procedures into low-level instruction sequences
Assembly Basics: Registers, operands, move
  The x86-64 move instructions cover wide range of data movement forms
Arithmetic
  C compiler will figure out different instruction combinations to carry out computation