## Slide 1: 无线传感器网络 Wireless Sensor Networks
2019年高新“标杆课程”项目
计算机学院 刘 亮

## Slide 2: Chapter I Motivation for a Network of Wireless Sensor Nodes

## Slide 3: Outline
Definitions and background
Challenges and constraints
Overview of topics covered

## Slide 4: Sensing and Sensors
Sensing: technique to gather information about physical objects or areas
Sensor (transducer): object performing a sensing task; converting one form of energy in the physical world into electrical energy
Examples of sensors from biology: the human body
  eyes: capture optical information (light)
  ears: capture acoustic information (sound)
  nose: captures olfactory information (smell)
  skin: captures tactile information (shape, texture)

## Slide 5: Sensing (Data Acquisition)
Sensors capture phenomena in the physical world (process, system, plant)
Signal conditioning prepare captured signals for further use (amplification (放大), attenuation (衰减), filtering of unwanted frequencies...)
Analog-to-digital conversion (ADC) translates analog signal into digital signal
Digital signal is processed and output is often given (via digital-analog converter and signal conditioner) to an actuator (device able to control the physical world)

## Slide 6: Sensor Classifications
Physical property to be monitored determines type of required sensor
辐射
电磁的
机械的

## Slide 7: Other Classifications
Power supply:
  active sensors require external power, i.e., they emit energy (microwaves, light, sound) to trigger response or detect change in energy of transmitted signal (e.g., electromagnetic proximity sensor)
  passive sensors detect energy in the environment and derive their power from this energy input (e.g., passive infrared (红外) sensor)

## Slide 8: Other Classifications
  Electrical phenomenon:
resistive sensors (电阻式传感器) use changes in electrical resistivity (ρ) based on physical properties such as temperature (resistance R = ρ*l/A)
capacitive sensors (电容式传感器) use changes in capacitor dimensions or permittivity (电容率) (ε) based on physical properties (capacitance C = ε*A/d)
inductive sensors (电感式传感器) rely on the principle of inductance（感应系数）(electromagnetic force is induced by fluctuating current)
piezoelectric sensors（压电传感器）rely on materials (crystals, ceramics) that generate a displacement of charges in response to mechanical deformation

## Slide 9: Wireless Sensor Network (WSN)
Multiple sensors form a network to cooperatively monitor large or complex physical environments
Acquired information is wirelessly communicated to a base station (BS), which propagates the information to remote devices for storage, analysis, and processing

## Slide 10: History of Wireless Sensor Networks
DARPA:
  Distributed Sensor Nets Workshop (1978)
  Distributed Sensor Networks (DSN) program (early 1980s)
  Sensor Information Technology (SensIT) program

## Slide 11: History of Wireless Sensor Networks
  UCLA and Rockwell Science Center
  Wireless Integrated Network Sensors (WINS)
  Low Power Wireless Integrated Microsensor (LWIM) (1996)
  UC-Berkeley
  Smart Dust project (1999)
  concept of “motes”: extremely small sensor nodes
  Berkeley Wireless Research Center (BWRC)
  PicoRadio project (2000)
  MIT
  μAMPS (micro-Adaptive Multidomain Power-aware Sensors) (2005)

## Slide 12: History of Wireless Sensor Networks
Commercial efforts
  Crossbow (www.xbow.com)
  Sensoria (www.sensoria.com)
  Worldsens (worldsens.citi.insa-lyon.fr)
  Dust Networks (www.dustnetworks.com)
  Ember Corporation (www.ember.com)

## Slide 13: WSN Communication
Characteristics of typical WSN:
  low data rates
  energy-constrained sensors
  IEEE 802.11 family of standards
  most widely used WLAN protocols for wireless communications in general
  can be found in early sensor networks or sensors networks without stringent energy constraints
  IEEE 802.15.4 is an example for a protocol that has been designed specifically for short-range communications in WSNs
  low data rates
  low power consumption
  widely used in academic and commercial WSN solutions

## Slide 14: Single-Hop versus Multi-Hop
Star topology
  every sensor communicates directly (single-hop) with the base station
  may require large transmit powers and may be infeasible in large geographic areas
  Mesh topology
  sensors serve as relays (forwarders) for other sensor nodes (multi-hop)
  may reduce power consumption and allows for larger coverage
  introduces the problem of routing

## Slide 15: Outline
Definitions and background
Challenges and constraints
Overview of topics covered

## Slide 16: Challenges in WSNs: Energy
Sensors typically powered through batteries
  replace battery when depleted
  recharge battery, e.g., using solar power
  discard sensor node when battery depleted
For batteries that cannot be recharged, sensor node should be able to operate during its entire mission time or until battery can be replaced
Energy efficiency is affected by various aspects of sensor node/network design

## Slide 17: Challenges in WSNs: Energy
Physical layer:
  switching and leakage energy of CMOS-based processors
Medium access control layer:
  contention-based strategies lead to energy-costly collisions
  problem of idle listening
Network layer:
  responsible for finding energy-efficient routes

## Slide 18: Challenges in WSNs: Energy
Operating system:
  small memory footprint and efficient task switching
Security:
  fast and simple algorithms for encryption (加密), authentication（鉴定）, etc.
Middleware:
  in-network processing of sensor data can eliminate redundant data or aggregate sensor readings

## Slide 19: Challenges in WSNs: Self-Management
Ad-hoc deployment
many sensor networks are deployed “without design”
  sensors dropped from airplanes (battlefield assessment)
  sensors placed wherever currently needed (tracking patients in disaster zone)
  moving sensors (robot teams exploring unknown terrain)
sensor node must have some or all of the following abilities
  determine its location
  determine identity of neighboring nodes
  configure node parameters
  discover route(s) to base station
  initiate sensing responsibility

## Slide 20: Challenges in WSNs: Self-Management
Unattended operation
once deployed, WSN must operate without human intervention
device adapts to changes in topology, density, and traffic load
device adapts in response to failures
  Other terminology
self-organization is the ability to adapt configuration parameters based on system and environmental state
self-optimization is the ability to monitor and optimize the use of the limited system resources
self-protection is the ability recognize and protect from intrusions and attacks
self-healing is the ability to discover, identify, and react to network disruptions

## Slide 21: Challenges in WSNs: Wireless Networks
Attenuation（衰减）
  limits radio range
    Multi-hop communication
  increased latency
  increased failure/error probability
  complicated by use of duty cycles

## Slide 22: Challenges in WSNs: Decentralization
    Centralized management (e.g., at the base station) of the network often not feasible due to large scale of network and energy constraints
    Example: routing
    Centralized:
      BS collects information from all sensor nodes
      BS establishes “optimal” routes (e.g., in terms of energy)
      BS informs all sensor nodes of routes
      can be expensive, especially when the topology changes frequently
    Decentralized:
      each sensor makes routing decisions based on limited local information
      routes may be non-optimal, but route establishment/management can be much cheaper

## Slide 23: Challenges in WSNs: Design Constraints
    Many hardware and software limitations affect the overall system design
    Examples include:
  Low processing speeds (to save energy)
  Low storage capacities (to allow for small form factor and to save energy)
  Lack of I/O components such as GPS receivers (reduce cost, size, energy)
  Lack of software features such as multi-threading (reduce software complexity)

## Slide 24: Challenges in WSNs: Security
    Sensor networks often monitor critical infrastructure or carry sensitive information, making them desirable targets for attacks
    Attacks may be facilitated by:
  remote and unattended operation
  wireless communication
  lack of advanced security features due to cost, form factor, or energy
    Conventional security techniques often not feasible due to their computational, communication, and storage requirements
    As a consequence, sensor networks require new solutions for intrusion detection, encryption, key establishment and distribution, node authentication, and secrecy

## Slide 25: Comparison

## Slide 26: Outline
Definitions and background
Challenges and constraints
Overview of topics covered

## Slide 27: Overview of topics covered
  Part One: Introduction
  1 Motivation for a Network of Wireless Sensor Nodes
  2 Applications
  3 Node Architecture
  4 Operating Systems
    Part Two: Basic Architecture Framework
  5 Physical Layer
  6 Medium Access Control
  7 Network Layer

## Slide 28: Overview of topics covered
  Part Three: Node and Network Management
  8 Power Management
  9 Time Synchronization
  10 Localization
  11 Coverage
  Part Four: Other Specific Types of WSN
  12 Multimedia Sensor Networks
  13 Mobile Crowd-Sensing Networks

## Slide 29: Chapter 2 Applications

## Slide 30: Outline
Structural Health Monitoring
  Wisden
  Golden Gate Bridge
Traffic Control
  Knaian (2000)
  Arora (2004)
Precision Agriculture
  Wine Vinyard (2004)
  Lofar Agro (2005)
  Active Volcano
  Volcán Tungurahua

## Slide 31: Structural Health Monitoring
Motivation:
  Events:
    On August 2, 2007, a highway bridge unexpectedly collapsed in Minnesota
    Nine people were killed in the event
    Potential causes: wear and tear, weather and the weight of a nearby construction project
    In fact, the BBC reported (August 14, 2007) that China had identified more than 6,000 bridges that were damaged or considered to be dangerous
  These accidents motivate wireless sensor networks for monitoring bridges and similar structures

## Slide 32: Structural Health Monitoring
Traditionally Inspections:
  Visual Inspection : everyday
  Labor-intensive, tedious, inconsistent and subjective
  Basic Inspections : at least once a year
  Detailed Inspection : at least every five years on selected bridges
  Special Inspections : according to technical needs
  The rest require sophisticated tools: expensive, bulky and power consuming

## Slide 33: Local and Global Inspections
Local inspection techniques focus on detecting highly localized, imperceptible fractures in a structure
  Requires:
    A significant amount of time
    The disruption of the normal operation of the structure
Global inspection techniques aim to detect a damage or defect that is large enough to affect the entire structure
  Researcher have been developing and testing wireless sensor networks as global inspection techniques

## Slide 34: Wisden
The first prototype to employ WSN for monitoring structural health
  First deployment ---- for conducting seismic experiments
    On an imitation of a full-scale 28×28 square foot hospital ceiling
    The overall weight which the ceiling supports is approximately 12,000 pounds
  Second deployment
    25 nodes (a tree topology) and a 16 bit vibration card
    A high-sensitive triaxial accelerometer (三轴加速器) is attached to the vibration card
    Designed for high-quality, low-power vibration sensing
    The task of the network was to reliably send time-synchronized vibration data to a remote sink over a multi-hop route

## Slide 35: Golden Gate Bridge (Univ. of California)

## Slide 36: Golden Gate Bridge
64 wireless sensor nodes deployed on this bridge
The network monitors ambient vibrations synchronously
  1 KHz rate, ≤10μs jitter, accuracy=30μG, over a 46 hop network
The goal of the deployment:
  Determine the response of the structure to both ambient and extreme conditions
  Compare actual performance to design predictions
  Measure ambient structural accelerations from wind load
  Measure strong shaking from a potential earthquake
  The installation and the monitoring was conducted without the disruption of the bridge’s operation

## Slide 37: Outline
Structural Health Monitoring
  Wisden
  Golden Gate Bridge
Traffic Control
  Knaian (2000)
  Arora (2004)
Precision Agriculture
  Wine Vinyard (2004)
  Lofar Agro (2005)
  Active Volcano
  Volcán Tungurahua

## Slide 38: Traffic Control
Motivation:
  Ground transportation is a vital and a complex socio-economic infrastructure
    it is linked with and provide support for a variety of systems, such as supply-chain, emergency response and public health
    The 2009 Urban Mobility Report, reveals that in 2007, congestion caused urban Americans to
      Travel 4.2 billion hours more
      Purchase an extra 2.8 billion gallons of fuel
    Congestion cost is very high ---- $87.2 billion an increase of more than 50% over the previous decade

## Slide 39: Traffic Control
Motivation:
  Building new roads is not a feasible solution for many cities
    the lack of free space
    the high cost of demolition of old roads
  One approach: put in place distributed systems that reduce congestions
    Gather information about the density, sizes and speed of vehicles on roads
    Infer congestions
    Suggest to drivers alternative routes and emergency exits

## Slide 40: The Sensing Task
Inductive Loops (in-road sensing devices)
  Advantages:
    Unaffected by weather
    Provide direct information (few ambiguity)
  How does it work: using Faraday’s induction law
    A coil of wire (several meters in diameter, passes an electric current through the coil)
    It can be buried under the road and connected to a roadside control box
    A magnetic field strength can be induced as a result of a current and the speed and the size of passing vehicles

## Slide 41: Magnetic Sensors
Magnetic sensors can determine the direction and speed of a vehicle
  A moving vehicle can disturb the distribution of the magnetic field
    By producing its own magnetic field
    By cutting across it
The magnitude and direction of the disturbance depends on
  The speed, size, density and permeability（导磁系数）of the vehicle
Classification of Magnetic sensors:
  Low field ( below 1μGauss)
  Medium field ( between 1μGauss and 10μGauss)
  High field ( above 10μGauss)

## Slide 42: Magnetic Sensors
Detection of a moving vehicle with an ARM magnetic sensor (Caruso and Withanawasam 1999)

## Slide 43: Magnetic Sensors
Almost all road vehicles contain a large mass of steel
The magnetic permeability (磁导系数) of steel is much higher than the surrounding air
Steel has the capacity to concentrate the flux lines of the Earth’s magnetic field
The concentration of magnetic flux varies as the vehicle moves; it can be detected from a distance of up to 15m
The field variation reveals a detailed magnetic signature
It is possible to distinguish between different types of vehicles

## Slide 44: Knaian (2000)
Block diagram of the MIT node for traffic monitoring
(Knaian 2000)

## Slide 45: Knaian (2000)
The node consists of
  Two AMR magnetic sensors to detect vehicular activities
    By observing the disturbance in the Earth’s magnetic field the vehicular creates
    The vehicle pulls field lines away from the sensor when it approaches it
    Then towards the sensor when it drives away from it
  A temperature sensor to monitor road condition (snow, ice, or water)

## Slide 46: Knaian (2000)
To measure the speed of a vehicle, the node waits until it detects an excursion from the predefined baseline and then starts sampling at a frequency of 2KHz
  Two AMR magnetic sensors are placed one at the front of the node and the other at the back ---- they are shifted in time
  The node waits for the signal from the rear sensor to cross the baseline
  Then it begins to count the number of samples until the signal from the forward sensor crosses the baseline
  From this count, it computes the speed of the passing vehicle

## Slide 47: Arora et al.(2004)
It deploy 90 sensor nodes to detect the movement of vehicles, soldiers and people
  78 of the nodes were magnetic sensor nodes that were deployed in a 60×25 square foot area
  12 radar sensor nodes were overlaid on the network
These nodes form a self-organizing network which connects itself to a remote computer via a base station and a long haul radio repeater

## Slide 48: Outline
Structural Health Monitoring
  Wisden
  Golden Gate Bridge
Traffic Control
  Knaian (2000)
  Arora (2004)
Precision Agriculture
  Wine Vinyard (2004)
  Lofar Agro (2005)
  Active Volcano
  Volcán Tungurahua

## Slide 49: Precision Agriculture
Motivation:
  A large farm is taken resource distribution and its response to climate change, weeds and pests
  Accordingly, farmers administer
    Fertilizers (肥料), pesticides (农药), and water resources
  In reality, wide spatial diversity in soil types, nutrient content and other important factors
  Therefore, treating it as a uniform field can cause
    Inefficient use of resources
    Loss of productivity
Precision agriculture is a method of farm management that enables farmers to produce more efficiently through a frugal use of resources

## Slide 50: Precision Agriculture
Precision agriculture technologies:
  Yield monitors
  Yield mapping
  Variable rate fertilizer
  Weed mapping
Requirements of precision agriculture technologies:
  Collect a large amount of data
  Over several days
  Variable spraying
  Topography and boundaries
  Salinity mapping
  Guidance systems

## Slide 51: Wine Vinyard (2004)
Motivation:
  In a vineyard, temperature is the predominant climate that affects the quality as well as the quantity of harvest
  Wine grapes see no real growth until the temperature goes above 10°C
  Different wine grapes have different requirements for heat units
  Subsequently, the deployment aims to
    Measure the temperature over a 10°C baseline that a site accumulates over the growing season

## Slide 52: Wine Vinyard (2004)
Beckwith et al. deploy a WSN to monitor and characterize variation in temperature of a wine vineyard
  Heat summation and periods of freezing temperatures
65 nodes in a grid like pattern 10 to 20 meters apart, covering about two acres
Easy to develop the network(1 person day)
  Due to self-configuration nature of the network
  Inherent structured layout of vineyard fields
Two essential constraints of the network topology
  Placement of nodes in an area of viticulture interest
  The support for multi-hop communication

## Slide 53: Wine Vinyard (2004)
The data were used to investigate several aspects:
  The existence of co-variance between the temperature data collected by the network
  Growing degree day differences
  Potential frost damage
The mean data enabled to observe the relative differences between heat units accumulation during that period
  According to the authors’ report, the extent of variation in this vineyard – there was a measured difference of over 35% of heat summation units (HSUs) in as little as 100 meters

## Slide 54: Lofar Agro (2005)
Baggio deploy a WSN at Lofar Agro, the Netherlands.
The network was tasked to monitor phytophthora
  Phytophthora is a fungal disease in a potato field
Climatologically conditions are the main cause to phytophthora
  Thus, observing the humidity and temperature conditions in the field
  Observing the wetness of the potato leaves
  To determine the potential risk of the disease and the requirements for fungicide

## Slide 55: Lofar Agro (2005)
Implementation:
  150 wireless sensor nodes (20, 40 and 60 cm)
    Temperature and humidity sensors
  Additional 30 nodes (75 cm) to ensure the network’s connectivity
    The radio range of the nodes reduced when the potato crop was flowering
  The nodes sampled temperature and humidity at a rate of 1 sample per minute and stored the result temporarily
  The data were communicated to a remote base station every 10 minutes

## Slide 56: Lofar Agro (2005)
Implementation:
  Delta encoding and periodic sleeping to efficiently utilize energy
    Delta encoding: ten samples were encoded in a single packet
  The sampled data were logged to a server
  The server filtered out erroneous readings and handed the accumulated data to the Phytophthora decision support system (DSS) server
  Finally, the decision support system combined the field data with a detailed weather forecast to determine the treatment policy

## Slide 57: Outline
Structural Health Monitoring
  Wisden
  Golden Gate Bridge
Traffic Control
  Knaian (2000)
  Arora (2004)
Precision Agriculture
  Wine Vinyard (2004)
  Lofar Agro (2005)
  Active Volcano
  Volcán Tungurahua

## Slide 58: Active Volcano
Volcanoes occur when broken slabs of the Earth’s outermost shell -- collide
  Float on the hotter and softer layer in the Earth’s mantle
Motivation:
  The Earth’s volcanoes are hidden from view
  Occurring on the ocean floor along spreading ridges
  At present, typical active volcanoes are monitored by expensive devices that are difficult to move or require external supply voltage
  The deployment and maintenance of these devices require vehicle or helicopter assistance
  Data storage must be retrieved on a periodic basis

## Slide 59: Active Volcano
WSN can be very useful for active volcano monitoring
  A large number of small, cheap and self-organizing nodes
  They can be deployed to cover a vast field
Advantage of WSN in active volcano monitoring
  Fast and economical deployment
  Possible to achieve high spatial diversity
  The networks can operate without requiring stringent maintenance routines

## Slide 60: Volcán Tungurahua
Volcán Tungurahua in central Ecuador(2004)
  3 sensor nodes
  Integrate microphones
Volcán Reventador in northern Ecuador(2005)
  16 sensor nodes
  Integrate seism acoustic sensors
  Linear topology (3km)

## Slide 61: Volcán Tungurahua
An important task in active volcano monitoring is to capture discrete events
  Eruptions, earthquakes, or tremor activities
  These events are transient
  Having duration of less than 60 seconds
  Occurring several times a day
The researchers employed the raw data to investigate volcanic activities
  The samples must be accurately time stamped to allow comparisons between correlated measurements

## Slide 62: Volcán Tungurahua
The sensor architecture consisted of
  An 8dBi 2.4GHz external omnidirectional antenna
  A seismometer
  A microphone
  A custom hardware interface board
Operating environment ---- TinyOS
The flash memory ---- for buffering raw data
Conclusion
  WSN are suitable for capturing triggered events
  WSN are inadequate for capturing complete waveforms for a long time

## Slide 63: Wireless Sensor Network Based Mobile Pet

## Slide 64: Chapter 3 Node Architecture

## Slide 65: Outline
Node Architecture
The Sensing Subsystem
The Processor Subsystem
Communication Interfaces
Prototypes

## Slide 66: Node Architecture
Wireless sensor nodes are the essential building blocks in a wireless sensor network
  Sensing, processing and communication take place through a node
  Stores and executes the communication protocols as well as data processing algorithms
The node consists of sensing, processing, communication and power subsystems
  Trade-off between flexibility and efficiency – both in terms of energy and performance

## Slide 67: Node Architecture
Architecture of a wireless sensor node

## Slide 68: Outline
Node Architecture
The Sensing Subsystem
The Processor Subsystem
Communication Interfaces
Prototypes

## Slide 69: The Sensing Subsystem
The sensing subsystem integrates

## Slide 70: The Sensing Subsystem
The sensing subsystem integrates

## Slide 71: The Sensing Subsystem
The sensing subsystem integrates

## Slide 72: Analog-to-Digital Converter
ADC converts the output of a sensor ---- which is a continuous, analog signal ---- into a digital signal.
It requires two steps:
Step1: The analog signal has to be quantized (量化)
Allowable discrete values is influenced :
    a) By the frequency and magnitude of the signal
    b) By the available processing and storage resources

## Slide 73: Analog-to-Digital Converter
Step2: The sampling frequency (采样)
  Nyquist rate does not suffice because of noise and transmission error
  Resolution of ADC -- An expression of the number of bits that can be used to encode the digital output
  where Q is the resolution in volts per step (volts per output code); Epp is the peak-to-peak analog voltage; M is the ADC’s resolution in bits

## Slide 74: Outline
Node Architecture
The Sensing Subsystem
The Processor Subsystem
Communication Interfaces
Prototypes

## Slide 75: The Processor Subsystem
The processor subsystem
  Interconnects all the other subsystems and some additional peripheries
  Its main purpose is to execute instructions pertaining to sensing, communication and self-organization
It consists
  A processor chip
  A nonvolatile memory ---- stores program instructions
  An active memory ---- temporarily stores the sensed data
  An internal clock

## Slide 76: Architectural Overview
The processor subsystem can be designed by employing one of the three basic computer architectures
  Von Neumann architecture
  Harvard architecture
  Super-Harvard (SHARC) architecture

## Slide 77: Von Neumann Architecture
Von Neumann architecture
  provides a single memory space ---- storing program instructions and data
  provides a single bus ---- to transfer data between the processor and the memory
  Slow processing speed ---- each data transfer requires a separate clock

## Slide 78: Harvard Architecture
Provides separate memory spaces ---- storing program instructions and data
Each memory space is interfaced with the processor with a separate data bus
Program instructions and data can be accessed at the same time
A special Single instruction, multiple data (SIMD) operation, a special arithmetic operation and a Bit reverse. Supports multitasking operating systems; but does not provide virtual memory protection

## Slide 79: Super-Harvard Architecture
  Internal instruction cache ---- temporarily store frequently used instructions ---- enhances performance
    An underutilized program memory can be used as a temporary relocation place for data
An extension of the Harvard architecture, adds two components:
  Direct Memory Access (DMA)
    The costly CPU cycles can be invested in a different task
    Program memory bus and data memory bus accessible from outside the chip

## Slide 80: Microcontroller
Structure of Microcontroller
  A CPU core
  A volatile memory (RAM) for data storage
  A ROM, EPROM, EEPROM or Flash memory
  Parallel I/O interfaces
  Discrete input and output bits
  A clock generator
  One or more internal analog-to-digital converters
  Serial communications interfaces

## Slide 81: Microcontroller
Advantages:
  It suitable for building computationally less intensive, standalone applications, because of its compact construction, small size, low-power consumption and low cost
  High speed of the programming and eases debugging, because of the use of higher-level programming languages
Disadvantages:
  Not as powerful and as efficient as some custom-made processors (such as DSPs and FPGAs)
  Some applications (simple sensing tasks but large scale deployments) may prefer to use architecturally simple but energy and cost efficient processors

## Slide 82: Digital Signal Processor
The main function:
  Process discrete signals with digital filters
  Filters minimize the effect of noise on a signal or enhance or modify the spectral characteristics of a signal
  While analog signal processing requires complex hardware components, digital signal process (DSP) requires simple adders, multipliers, and delay circuits
  DSPs are highly efficient
  Most DSPs are designed with the Harvard Architecture

## Slide 83: Digital Signal Processor
Advantages:
  Powerful and complex digital filters can be realized with commonplace DSPs
  Useful for applications that require the deployment of nodes in harsh physical settings (where the signal transmission suffers corruption due to noise and interference and, hence, requires aggressive signal processing)
Disadvantage:
  Some tasks require protocols (and not numerical operations) that require periodical upgrade or modifications (i.e., the networks should support flexibility in network reprogramming)

## Slide 84: Application-specific Integrated Circuit
ASIC is an IC that can be customized for a specific application
Two types of design approaches: fully customized and half-customized
  A full-customized IC:
    some logic cells, circuits, or layout are custom made in order to optimize cell performance
    Includes features which are not defined by the standard cell library
    Expensive and long design time
  A half-customized ASIC is built with logic cells that are available in the standard library
  In both cases, the final logic structure is configured by the end user ---- An ASIC is a cost efficient solution, flexible and reusable

## Slide 85: Application-specific Integrated Circuit
Advantages:
  Relatively simple design; can be optimized to meet a specific customer demand
  Multiple microprocessor cores and embedded software can be designed in a single cell
Disadvantage:
  High development costs and lack of re-configurability
Application:
  ASICs is not to replace microcontrollers or DSPs but to complement them
  Handle rudimentary and low-level tasks
    To decouple these tasks from the main processing subsystem

## Slide 86: Field Programmable Gate Array (FPGA)
The distinction between ASICs and FPGAs is not always clear
  FPGAs are more complex in design and more flexible to program
  FPGAs are programmed electrically, by modifying a packaged part
  Programming is done with the support of circuit diagrams and hardware description languages, such as VHDL and Verilog

## Slide 87: Field Programmable Gate Array (FPGA)
Advantages:
  Higher bandwidth compared to DSPs
  Flexible in their application
  Support parallel processing
  Work with floating point representation
  Greater flexibility of control
Disadvantages:
  Complex
  The design and realization process is costly

## Slide 88: Comparison
Working with a micro-controller is preferred if the design goal is to achieve flexibility
Working with all the other is preferred if power consumption and computational efficiency is desired
DSPs are expensive, large in size and less flexible; they are best for signal processing, with specific algorithms

## Slide 89: Comparison
FPGAs are faster than both microcontrollers and digital signal processors and support parallel computing; but their production cost and the difficulty with programming make them less suitable
ASICs have higher bandwidths; they are the smallest in size, perform much better and consume less power than any of the other processing types; but have a high cost of production owing to the complex design process

## Slide 90: Outline
Node Architecture
The Sensing Subsystem
The Processor Subsystem
Communication Interfaces
Prototypes

## Slide 91: Communication Interfaces
Fast and energy efficient data transfer between the subsystems of a wireless sensor node is vital
  However, the practical size of the node puts restriction on system buses
  Communication via a parallel bus is faster than a serial transmission
  A parallel bus needs more space
Therefore, considering the size of the node, parallel buses are never supported

## Slide 92: Communication Interfaces
The choice is often between serial interfaces:
  Serial Peripheral外围 Interface (SPI)
  General Purpose Input/Output (GPIO)
  Secure Data Input/Output (SDIO)
  Inter-Integrated Circuit (I2C)
Among these, the most commonly used buses are SPI and I2C

## Slide 93: Serial Peripheral Interface
SPI (Motorola, in the mid of the 1980s)
  A high-speed, full-duplex synchronous serial bus
  Does not have an official standard, but use the SPI interface should conform to the implementation specification of others ---- correct communication
The SPI bus defines four pins:
  MOSI (MasterOut/SlaveIn)
    It is used to transmit data from the master to the slave when a device is configured as a master
  MISO (MasterIn/SlaveOut)
  SCLK (Serial Clock)
    By the master to send the clock signal that is needed to synchronize transmission
    By the slave to read this signal synchronize transmission
  CS (Chip Select) ---- communicate via the CS port

## Slide 94: Serial Peripheral Interface
Both master and slave devices hold a shift register
Every device in every transmission must read and send data
SPI supports a synchronous communication protocol
  The master and the slave must agree on the timing
  Master and slave should agree on two additional parameters
    Clock polarity (CPOL) ---- defines whether a clock is used as high- or low-active
    Clock phase (CPHA) ---- determines the times when the data in the registers is allowed to change and when the written data can be read

## Slide 95: Serial Peripheral Interface

## Slide 96: Inter-Integrated Circuit

## Slide 97: Inter-Integrated Circuit
Every device type that uses I2C must have a unique address that will be used to communicate with a device
In earlier versions, a 7 bit address was used, allowing 112 devices to be uniquely addressed ---- due to an increasing number of devices, it is insufficient
Currently I2C uses 10 bit addressing
I2C is a multi-master half-duplex synchronous serial bus
  Only two bidirectional lines: (unlike SPI, which uses four)
    Serial Clock (SCL)
    Serial Data (SDA)

## Slide 98: Inter-Integrated Circuit
Since each master generates its own clock signal, communicating devices must synchronize their clock speeds
  A slower slave device could wrongly detect its address on the SDA line while a faster master device is sending data to a third device
I2C requires arbitration between master devices wanting to send or receive data at the same time
  No fair arbitration algorithm
  Rather the master that holds the SDA line low for the longest time wins the medium？

## Slide 99: Inter-Integrated Circuit
I2C enables a device to read data at a byte level for a fast communication
  the device can hold the SCL low until it completes reading or sending the next byte ---- it is called handshaking
The aim of I2C is to minimize costs for connecting devices
  Accommodating lower transmission speeds
I2C defines two speed modes:
  A Fast-mode ---- a bit rate of up to 400Kbps
  High-speed mode ---- a transmission rate of up to 3.4 Mbps
  They are downwards compatible to ensure communication with older components

## Slide 100: Inter-Integrated Circuit

## Slide 101: Comparison

## Slide 102: Communication Interfaces
Buses are essential highways to transfer data
  Due to the concern for size, only serial buses can be used
  Serial buses demand high clock speeds to gain the same throughput as parallel buses
  Serial buses can also be bottlenecks (e.g.. Von Neumann architecture) or may not scale well with processor speed (e.g.. I2C)
Delays due to contention for bus access become critical, for example, if some of the devices act unfairly and keep the bus occupied

## Slide 103: Outline
Node Architecture
The Sensing Subsystem
The Processor Subsystem
Communication Interfaces
Prototypes

## Slide 104: The IMote Node Architecture
The IMote sensor node architecture is a multi-purpose architecture, consisting of :
  A power management subsystem
  A processor subsystem
  A sensing subsystem
  A communication subsystem
  An interfacing subsystem

## Slide 105: The IMote Node Architecture
A multiple sensor board contains :
  A 12-bit, four channels ADC
  A high-resolution temperature/humidity sensor
  A low-resolution digital temperature sensor
  A light sensor
  The I2C bus is chosen to connect low data rate sources
  The SPI bus is used to interface high data rate sources

## Slide 106: The IMote Node Architecture
The processing subsystem provides
  A main processor (microprocessor)
    Operate at a low voltage (0.85V), low frequency (13MHz) mode
    Dynamic Voltage Scaling (104MHz ---- 416MHz)
    Sleep and deep sleep modes
    Thus enabling low power operation
  A coprocessor (a DSP)
    Accelerate multimedia operations ---- computation intensive

## Slide 107: The XYZ Node Architecture
  The power subsystem
  The communication subsystem
  The mobility subsystem
  The sensor subsystem
It consists of the four subsystems:

## Slide 108: The XYZ Node Architecture
The processor subsystem is based on the ARM7TDMI core microcontroller
  f max = 58MHz
  Two different modes (at 32bits and 16bits)
  Provides an on-chip memory of 4KB boot ROM and a 32KB RAM ---- can be extended by up to 512KB of flash memory
The peripheral components:
  A DMA controller
  Four 10-bit ADC inputs
  Serial ports (RS232, SPI, I2C, SIO)
  42 multiplexed general purpose I/O pins

## Slide 109: The XYZ Node Architecture
The communication subsystem connected to the processing subsystem through a SPI interface
  The CC2420 is a RF transceiver
  When an RF message has been successfully received
  The SPI interface enables the radio to wake up a sleeping processor
  The processor subsystem controls the communication subsystem by either turning it off or putting it in sleep mode

## Slide 110: The Hogthrob Node Architecture
It is designed for a specific application, namely, to monitor pig production
Motivation:
  Monitors movements between a sow and the onset of estrus, so that appropriate care can be given for pregnant sows
  Detecting cough or limping to monitor illness

## Slide 111: The Hogthrob Node Architecture
The processing subsystems consists of :
  A microcontroller
    Performs less complex, less energy intensive tasks
    Initializes the FPGA and functions as an external timer and an ADC converter to it
  A Field Programmable Gate Array
    Executes the sow monitoring application
    Coordinates the functions of the sensor node

## Slide 112: The Hogthrob Node Architecture
There are a number of interfaces supported by the processing subsystem, including
  The I2C interface for the sensing subsystem
  The SPI interface for the communication subsystem
  The JTAG interface for in-system programmability and debugging
  The serial (RS232) interface for interaction with a PC

## Slide 113: Chapter 4 Operating Systems

## Slide 114: Operating Systems
An operating System is
  a thin software layer
  resides between the hardware and the application layer
  provides basic programming abstractions to application developers
Its main task is to enable applications to interact with hardware resources

## Slide 115: Operating Systems
Operating systems are classified as: single-task/multitasking and single-user/multiuser operating systems!
  multi-tasking OS - the overhead of concurrent processing because of the limited resources!
  single task OS - tasks should have a short duration!
The choice of a particular OS depends on several factors; typically functional and non-functional aspects

## Slide 116: Outline
Functional Aspects
Non-Functional Aspects
Prototypes
Evaluation

## Slide 117: Outline
Functional Aspects
Non-Functional Aspects
Prototypes
Evaluation
  Data Types
  Scheduling
  Stacks
  System Calls
  Handling Interrupts
  Multithreading
  Thread-based vs. Event-based Programming
  Memory Allocation

## Slide 118: Data Types
Interactions between the different subsystems take place through:
  well-formulated protocols
  data types
Complex data types have strong expression power but consume resources - struct and enum
Simple data types are resource efficient but have limited expression capability - C programming language

## Slide 119: Scheduling
queuing-based scheduling
  FIFO - the simplest and has minimum system overhead, but treats tasks unfairly
  sorted queue - e.g., shortest job first (SJF) - incurs system overhead (to estimate execution duration)
round-robin scheduling
  a time sharing scheduling technique
  several tasks can be processed concurrently
Regardless of how tasks are executed, a scheduler can be either
  a non-preemptive scheduler - a task is executed to the end, may not be interrupted by another task
  or preemptive scheduler - a task of higher priority may interrupt a task of low priority

## Slide 120: Stacks & System Calls
Stacks
  a data structure that temporarily stores data objects in memory by piling one upon another
  objects are accessed using last-in-first-out (LIFO)
System Calls
  decouple the concern of accessing hardware resources from implementation details
  whenever users wish to access a hardware resource, they invoke these operations without the need to concern themselves how the hardware is accessed

## Slide 121: Handling Interrupts
An interrupt is an asynchronous signal generated by
  a hardware device
  several system events
  OS itself
An interrupt causes:
  the processor to interrupt executing the present instruction
  to call for an appropriate interrupt handler
Interrupt signals can have different priority levels, a high priority interrupt can interrupt a low level interrupt
Interrupt mask: let programs choose whether or not they wish to be interrupted

## Slide 122: Multi-threading
A thread is the path taken by a processor or a program during its execution
Multi-threading - a task is divided into several logical pieces
  scheduled independent from each other
  executed concurrently
Two advantages of a multi-threaded OS:
  tasks do not block other tasks
  short-duration tasks can be executed along with long-duration tasks
Keep the number of threads to a manageable size using a thread pool
  the creation of threads slows down the processor
  no sufficient resources to divide􀀁

## Slide 123: Thread-based vs Event-based Programming
Decision whether to use threads or events programming
  need for separate stacks
  need to estimate maximum size for saving context information
Thread-based programs use multiple threads of control within:
  a single program
  a single address space
  Advantage: a thread blocked can be suspended while other tasks are executed in different threads
  Disadvantages: 1) must carefully protect shared data structures with locks; 2) use condition variables to coordinate the execution of threads

## Slide 124: Thread-based vs Event-based Programming
In event-based programming: use events and event handlers
  event-handlers register with the OS scheduler to be notified when a named event occurs
  a loop function:
    polls for events
    calls the appropriate event-handlers when events occur
An event is processed to completion
  unless its handler reaches at a blocking operation (callback and returns control to the scheduler)

## Slide 125: Memory Allocation
How and for how long a memory is allocated for a piece of program determines the speed of task execution
Memory can be allocated to a program:
  statically - a frugal approach, but the requirement of memory must be known in advance
    memory is used efficiently
    runtime adaptation is not allowed
  dynamically - the requirement of memory is not known in advance (on a transient basis)
    enables flexibility in programming
    but produces a considerable management overhead

## Slide 126: Outline
Functional Aspects
Non-Functional Aspects
Prototypes
Evaluation
  Separation of Concern
  System Overhead
  Portability
  Dynamic Reprogramming

## Slide 127: Separation of Concern
Separation between the operating system and the applications layer
The operation systems can provide:
  a number of lightweight modules - “wired” together, or
  an indivisible system kernel + a set of library components for building an application, or
  a kernel + a set of reconfigurable low-level services
Separation of concern enables:
  flexible and efficient reprogramming and reconfiguration

## Slide 128: Portability
Ideally, operating systems should be able to co-exist and collaborate with each other
However, existing operating systems do not provide this type of support
In order to accommodate unforeseen requirements, operating systems should be portable and extensible

## Slide 129: System Overhead
An operating system executes program code – requires its own share of resources
The resources consumed by the OS are the system's overhead
  the size of the operating system
  the type of services that the OS provides to the higher-level services and applications
The resources of wireless sensor nodes have to be shared by programs that carry out:
  sensing, data aggregation, self-organization, network management, network communication

## Slide 130: Dynamic Reprogramming
Once a wireless sensor network is deployed, it may be necessary to reprogram some part of the application or the operating system for the following reasons:
  the network may not perform optimally
  both the application requirements and the network's operating environment can change over time
  may be necessary to detect and fix bugs􀀁

## Slide 131: Dynamic Reprogramming
Manual replacement may not be feasible - develop an operating system to provide dynamic reprogramming support, which depends on
  clear separation between the application and the OS
  the OS can receive software updates and assemble and store it in memory
  OS should make sure that this is indeed an updated version
  OS can remove the piece of software that should be updated and install and configure the new version
  all these consume resources and may cause their own bugs

## Slide 132: Dynamic Reprogramming
Software reprogramming (update) requires robust code dissemination protocols:
  splitting and compressing the code
  ensuring code consistency and version controlling
  providing a robust dissemination strategy to deliver the code over a wireless link

## Slide 133: Outline
Functional Aspects
Non-Functional Aspects
Prototypes
Evaluation
  TinyOS
  SOS
  Contiki
  LiteOS

## Slide 134: TinyOS
TinyOS is the most widely used, richly documented, and tool-assisted runtime environment in WSN
  static memory allocation
  event-based system
http://webs.cs.berkeley.edu/tos/

## Slide 135: TinyOS
TinyOSʼs architecture
  a scheduler
  a set of components, which are classified into
    configuration components - "wiring" (how modules are connected with each other)
    modules - the basic building blocks of a TinyOS program
Logical distinction between low-level and high-level components

## Slide 136: TinyOS
A component is made up of
  a frame
  command handlers
  event handlers
  a set of non-preemptive tasks
A component is similar to an object in object-based programming languages:
  it encapsulates state and interacts through well-defined interfaces
  an interface that can define commands, event handlers, and tasks

## Slide 137: TinyOS
Components are structured hierarchically and communicate with each other through commands and events:
  higher-level components issue commands to lower-level components
  lower-level components signal events to higher-level components
Two components at the highest level communicate asynchronously through active messages
  routing component - establishing and maintaining the network
  sensor application - responsible for sensing and processing

## Slide 138: TinyOS
The logical structure of components and component configurations
A TinyOS component providing an interface
A TinyOS component that uses an interface
A TinyOS configuration that wires an interface provider and an interface user
Component A declares its service by providing interface C, which in turn provides command D1 and signals event D2.
Component B expresses interest in interface C by declaring a call to command D1 and by providing an event handler to process event D2.
A binding between Component A and Component B is established through the Configuration E.

## Slide 139: Tasks, Commands and Events
The fundamental building blocks of a TinyOS runtime environment: tasks, commands, and events
  enabling effective communication between the components of a single frame
Tasks:
  monolithic processes 单独进程- should execute to completion – they cannot be preempted by other tasks, though they can be interrupted by events
  possible to allocate a single stack to store context information
  call lower level commands; signal higher level events; and post (schedule) other tasks
  scheduled based on FIFO principle (in TinyOS)􀀁

## Slide 140: Tasks, Commands and Events
Commands:
  non-blocking requests made by higher-level components to lower-level components
  split-phase operation:
    a function call returns immediately
    the called function notifies the caller when the task is completed
Events:
  events are processed by the event handler
  event handlers are called when hardware events occur
  an event handler may react to the occurrence of an event in different ways
    deposit information into its frame, post tasks, signal higher level events, or call lower level commands

## Slide 141: SOS (Han et al. 2005 )
The SOS operating system (Han et al. 2005)
  establishes a balance between flexibility and resource efficiency
  supports runtime reconfiguration and reprogramming
The SOS operating system consists of:
  a kernel :
    provides interfaces to the underlying hardware
    provides priority-based scheduling mechanism
    supports dynamic memory allocation
  a set of modules – can be loaded and unloaded - a position independent binary
    enables SOS to dynamically link modules with each other

## Slide 142: Interaction
messages (asynchronous communication)
  a message that originates from module A to module B
    the message goes through the scheduler
    the kernel calls the appropriate message handler in module B and passes the message to it
  direct calls to registered functions (synchronous communication)
  requires modules to register their public functions at the kernel – all modules can subscribe to these functions
    the kernel creates a function control block (FCB) to store key information about the function
    this information is used to:
      handle function subscription
      support dynamic memory management
      support runtime module update (replacement)

## Slide 143: Interaction
illustrates the two basic types of interactions between modules
Interaction through a function call is faster than message-based communication

## Slide 144: Dynamic Reprogramming
Five basic features enable SOS to support dynamic reprogramming
  modules are position independent binaries
    they use relative addresses rather than absolute addresses ---- they are re-locatable
  every SOS module implements two types of handlers – the init and final message handlers
    the init message handler - to set the moduleʼs initial state
    the final message handler - to release all resources the module owns and to enable the module to exit the system gracefully
    after the final message, the kernel performs garbage collection

## Slide 145: Dynamic Reprogramming
SOS uses a linker script to place the init handler of a module at a known offset in the binary
  enables easy linking during module insertion
SOS keeps the state of a module outside of it
  enables the newly inserted module to inherit the state information of the module it replaces
Whenever a module is inserted, SOS generates and keeps metadata that contains information:
  the ID of the module
  the absolute address of the init handler
  a pointer to the dynamic memory holding the module state

## Slide 146: Dynamic Reprogramming
In SOS, dynamic module replacement (update) takes place in three steps:
  a code distribution protocol advertises the new module in the network
  the protocol proceeds with downloading the module and examines the metadata
    the metadata contains the size of the memory required to store the local state of the module
    if a node does not have sufficient RAM, module insertion is immediately aborted
  if everything is correct, module insertion takes place and the kernel invokes the handler by scheduling an init message for the module􀀁

## Slide 147: Contiki
an event-driven kernel but multi-threading with a dynamic linking strategy
separate the kernel from processes
communication of services through the kernel by posting events
the kernel does not provide hardware abstraction
device drivers and applications communicate directly with the hardware
the kernel is easy to reprogram and it is easy to replace services

## Slide 148: Contiki
The Contiki operating system: the system programs are partitioned into core services and loaded programs

## Slide 149: Service Structure
Contiki OS supports
  dynamic loading
  reconfiguration of services
This is achieved by defining
  services
  service interfaces
  service stubs
  service layers
A Contiki service interaction architecture

## Slide 150: LiteOS
LiteOS is a thread-based operating system and supports multiple applications
  based on the principle of clean separation between the OS and the applications
  does not provide components or modules that should be “wired” together
  provides several system calls
  provides a shell - isolates the system calls from a user
  provides a hierarchical file management system
  provides a dynamic reprogramming technique

## Slide 151: LiteOS
The LiteOS operating system architecture (Cao et al. 2008)
LiteOS is modeled as a distributed file system

## Slide 152: Shell and System Calls
The shell provides:
  a mounting mechanism to a wireless node which is one-hop away from it
    a distributed and hierarchical file system
    a user can access the resources of a named node
  a large number of Linux commands
    file commands - move, copy and, delete files and directories
    process commands - manage threads
    debugging commands - set up a debugging environment and debug code
    environment commands
      user - managing the environment of OS
      manual - displaying interaction history and providing command reference
    device commands - provide direct access to hardware devices

## Slide 153: LiteFS
The file system structure of LiteFS (Cao et al. 2008)

## Slide 154: Dynamic Reprogramming
The LiteFS is a distributed file system
A user can
  access the entire sensor network
  program and manage individual nodes
LiteOS supports the dynamic replacement and reprogramming of user applications
  if the original source code is available to the OS
    recompiled with a new memory setting
    the old version will be redirected

## Slide 155: Dynamic Reprogramming
If the original source code is not available to the OS
  use a differential patching mechanism to replace an older version binary
    the start address (S) of the binary executable in the flash memory
    the start address of allocated memory in RAM (M)
    the stack top (T)
    T - M = the memory space allocated for the program code
  but the parameters are obtained empirically and require knowledge of the node architecture - limits the usefulness of the patching scheme

## Slide 156: Outline
Functional Aspects
Non-Functional Aspects
Prototypes
Evaluation

## Slide 157: Evaluation
Comparison of functional aspects of existing operating systems

## Slide 158: Evaluation
Comparison of nonfunctional aspects of existing operating systems

## Slide 159: Task I
PAPER READING: TinyOS An Operating System for Sensor Networks
Download and install TinyOS on your own laptop

## Slide 160: Chapter 5 Medium Access Control Layer

## Slide 161: Overview
Responsibilities of MAC layer include:
  decide when a node accesses a shared medium
  resolve any potential conflicts between competing nodes
  correct communication errors occurring at the physical layer
  perform other activities such as framing, addressing, and flow control
Second layer of the OSI reference or the IEEE 802 reference model

## Slide 162: Medium Access Control
In most networks, multiple nodes share a communication medium for transmitting their data packets
The medium access control (MAC) protocol is primarily responsible for regulating access to the shared medium
The choice of MAC protocol has a direct bearing on the reliability and efficiency of network transmissions
  due to errors and interferences in wireless communications and to other challenges
Energy efficiency also affects the design of the MAC protocol
  trade energy efficiency for increased latency or a reduction in throughput or fairness

## Slide 163: Outline
Wireless MAC protocols
Characteristics of MAC Protocols in Sensor Networks
Contention-Free MAC Protocols
Contention-Based MAC Protocols
Hybrid MAC Protocols

## Slide 164: MAC Protocol Categorization

## Slide 165: Contention-Free Medium Access
Collisions can be avoided by ensuring that each node can use its allocated resources exclusively
FDMA : Frequency Division Multiple Access
  the frequency band is divided into several smaller frequency bands
  the data transfer between a pair of nodes uses one frequency band
  all other nodes use a different frequency band
TDMA : Time Division Multiple Access
  multiple devices to use the same frequency band
  relies on periodic time windows ( frames)
    frames consist of a fixed number of transmission slots to separate medium accesses of different devices
    a time schedule indicates which node may transmit data during a certain slot

## Slide 166: Contention-Free Medium Access
CDMA : Code Division Multiple Access
  simultaneous accesses of the wireless medium are supported using different codes
  if these codes are orthogonal, it is possible for multiple communications to share the same frequency band
  forward error correction (FEC) at the receiver is used to recover from interferences among these simultaneous communications
Fixed assignment strategies are inefficient
  it is impossible to reallocate slots belonging to one device to other devices if not needed in every frame
    generating schedules for an entire network can be a taunting task
    these schedules may require modifications every time the network topology or traffic characteristics in the network change

## Slide 167: Contention-Free Medium Access
Dynamic assignment strategies: allow nodes to access the medium on demand
polling-based protocols
  a controller device issues small polling frames in a round-robin fashion, asking each station if it has data to send
  if no data to be sent, the controller polls the next station
  token passing
  stations pass a polling request to each other (round-robin fashion) using a special frame called a token
  a station is allowed to transmit data only when it holds the token
  reservation-based protocols
  static time slots used to reserve future access to the medium
  these often very complex protocols then ensure that other potentially conflicting nodes take note of such a reservation to avoid collisions

## Slide 168: Contention-Based Medium Access
Nodes may initiate transmissions at the same time
  requires mechanisms to reduce the number of collisions and to recover from collisions
Example 1: ALOHA protocol
  uses acknowledgments to confirm the success of a broadcast data transmission
    allows nodes to access the medium immediately
    addresses collisions with approaches such as exponential back-off to increase the likelihood of successful transmissions
Example 2: slotted-ALOHA protocol
  requires that a station may commence transmission only at predefined points in time (the beginning of a time slot)
  increases the efficiency of ALOHA
  introduces the need for synchronization among nodes

## Slide 169: Hidden and Exposed Terminal Problems
Hidden-terminal problem
  senders A and C are able to reach B, but cannot overhear each other ʼ s signals
  it is possible for A and C to transmit data to B at the same time, causing a collision at B, without being able to directly detect this collision
Exposed-terminal problem
  C wants to transmit data D, but decides to wait because it overhears an ongoing transmission from B to A
  Bʼ s transmission could not interfere with data reception at C

## Slide 170: Contention-Based Medium Access
CSMA with Collision Detection (CSMA/CD)
  sender first senses the medium to determine whether it is idle or busy
    if it is found busy, the sender refrains from transmitting packets
    if the medium is idle, the sender can initiate data transmission
  CSMA with Collision Avoidance (CSMA/CA)
  CSMA/CD requires that sender aware of collisions
  CSMA/CA attempts to avoid collisions in the first place

## Slide 171: Carrier Sense Multiple Access
Nodes first sense the medium before they begin a transmission (reduces number of collisions)
Non-persistent CSMA
  node is allowed to immediately transmit data once medium is idle
  if the medium is busy, the node performs a back-off operation
    wait for a certain amount of time before attempting to transmit again
1-persistent CSMA
  node wishing to transmit data continuously senses the medium for activity
  once the medium is found idle, the node transmits data immediately
  if a collision occurs, the node waits for a random period of time before attempting to transmit again

## Slide 172: Carrier Sense Multiple Access
p-persistent CSMA
  node continuously senses the medium
  node transmits data with a probability p once the medium becomes idle
  delays transmission with a probability 1 − p
  random back-off values are either continuous values in the case of un-slotted CSMA or multiples of a fixed slot size in slotted CSMA
CSMA/CA (CSMA with Collision Avoidance)
  nodes sense the medium, but do not immediately access the channel when it is found idle
  instead, a node waits for a time period called DCF interframe space (DIFS) plus a multiple of a slot size
  in case there are multiple nodes attempting to access the medium, the one with the shorter back-off period will win

## Slide 173: Carrier Sense Multiple Access
Example:
  node A waits for DIFS + 4 ∗ s (where s represents the slot size), while node Bʼ s back-off is DIFS + 7 ∗ s
  once node A begins with its transmission, node B freezes its own back-off timer and resumes the timer after node A completes its transmission plus another period of DIFS
  once node B ʼs back-off timer expires, it can also begin its transmission

## Slide 174: MACA and MACAW
Multiple Access with Collision Avoidance (MACA)
  dynamic reservation mechanism
  sender indicates desire to send with ready-to-send (RTS) packet
  intended receiver responds with clear-to-send (CTS) packet
  if sender does not receive CTS, it will retry at later point in time
  nodes overhearing RTS or CTS know that reservation has taken place and must wait (e.g., based on the size of data transmission)
  address hidden terminal problem and reduces number of collisions
MACA for Wireless LANs (MACAW)
  receiver responds with acknowledgment (ACK) after data reception
    other nodes in receiverʼs range learn that channel is available
  nodes hearing RTS, but not CTS do not know if transmission will occur
    MACAW uses data sending (DS) packet, sent by sender after receiving CTS to inform such nodes of successful handshake

## Slide 175: MACA By Invitation
In MACA-BI, destination device initiates data transfers by sending a Ready To Receive (RTR) packet to the source
  source then responds with the data message
Compared to MACA, MACA-BI reduces overhead
  increases the theoretical maximum throughput
  depends on the destination knowing when to receive data
Source nodes can use an optional field within the data message to indicate the number of queued messages
  providing the destination with an indication that more RTS packets will be required

## Slide 176: IEEE 802.11
Published in 1999 by the Institute of Electrical and Electronics Engineers
  specifies the physical and data link layers of the OSI model for wireless connections
Often referred to as Wireless Fidelity (Wi-Fi)
  certification given by Wi-Fi Alliance, a group that ensures compatibility between devices that use 802.11 standard
Wi-Fi combines concepts found in CSMA/CA and MACAW, but also offers features to preserve energy
Two modes of operation
  Point Coordination Function (PCF) mode
    communication among devices goes through a central entity called an access point (AP) or base station (BS) : managed mode
  Distributed Coordination Function (DCF) mode
    devices communicate directly with each other: ad-hoc mode

## Slide 177: IEEE 802.11
IEEE 802.11 is based on CSMA/CA
  before a node transmits, it first senses the medium for activity
  the node is allowed to transmit, if the medium is idle for at least a time period called the DCF interframe space (DIFS)
  otherwise the device executes a back-off algorithm to defer transmission to a later time
  this algorithm randomly selects a number of time slots to wait and stores this value in a back-off counter
  for every time slot that passes without activity on the network, the counter is decremented and the device can attempt transmission when this counter reaches zero
  if activity is detected before the counter reaches zero, the device waits until the channel has been idle for a period of DIFS before it continues to decrement the counter value

## Slide 178: IEEE 802.11
After a successful transmission
  receiver device responds with an acknowledgment after waiting for a time period called the short interframe space (SIFS)
  the value of SIFS is smaller than the value of DIFS to ensure that no other device accesses the channel before the receiver can transmit its acknowledgment
Once a node A makes a reservation using RTS and CTS control messages
  another neighboring node B, overhearing the RTS message, must refrain from accessing the medium until node A ʼ s transmission has been completed and acknowledged
  however, this would mean that node B has to continuously sense the medium to detect when it becomes idle again

## Slide 179: IEEE 802.11
Instead, A ’ s RTS message carries the size of the data it will transmit
  allowing node B to estimate how long the transmission will take and to decide whether to enter a low-power sleep mode
  some neighboring nodes may only overhear CTS (but not RTS), therefore, the data size is also carried in the CTS message
  using the data size information, neighboring nodes set a network allocation vector (NAV) that indicates how long the medium will be unavailable
    reduces the need for continuously sensing the medium, allowing a node to save power

## Slide 180: IEEE 802.11

## Slide 181: IEEE 802.11
PCF mode
  access point (AP) coordinates channel access to ensure collision-free communication
    periodically broadcasts a beacon to its client devices (includes list of devices with data pending at AP)
  during contention-free period, AP transmits these packets to its client devices
  AP can also poll client devices to allow them to initiate data transfers
  AP uses a wait period called the PCF interframe space (PIFS)
    PIFS is shorter than DIFS, but longer than SIFS
    ensures that PCF traffic has priority over traffic generated by devices operating in the DCF mode, without interfering with control messages in the DCF mode such as CTS and ACK

## Slide 182: IEEE 802.11
Focus of IEEE 802.11 is on providing fair access to the medium with support for high throughput and mobility
  since devices spend a large amount of time listening to the medium and collisions occur frequently, this standard incurs large overheads, including significant energy costs
Energy consumption problem
  IEEE 802.11 offers a power saving mode (PSM) for devices operating in the PCF mode
  devices can inform the AP that they wish to enter a low-power sleep mode using special control messages
  these devices wake up periodically to receive beacon messages from the AP to determine if they should stay awake to receive incoming messages
  saves energy, but only works in the infrastructure mode and it is not specified when or how long devices should sleep

## Slide 183: IEEE 802.15.4 & ZigBee
IEEE 802.15.4
  created for low-power devices in the 868 MHz, 915 MHz, and 2.45 GHz frequency bands
  supports two transmission modes :
    UWB PHY
      bit rates: 110 kbps, 851 kbps (nominal), 6.81 kbps, and 27.24 Mbps
    CSS PHY
      bit rates: 1 Mbps (nominal) and 250 kbps
Before 802.15.4, ZigBee Alliance worked on low-cost communication technology for low data rates and low power consumption
IEEE and ZigBee Alliance joined forces and ZigBee has become the commercial name for the IEEE 802.15.4 technology

## Slide 184: ZigBee
Star mode:
  communication via the Personal Area Network (PAN) coordinator
  synchronized mode (beacon-enabled)
    PAN coordinator periodically broadcasts beacons for synchronization and management
    slotted channel access: device performs random backoff before channel is sensed
      if no activity, node waits until next slot and senses channel again until no activity has been detected for two consecutive slots
      if activity, backoff procedure is repeated
  unsynchronized mode: device access channel immediately when no activity is detected during the first initial backoff time

## Slide 185: ZigBee
Peer-to-peer mode:
  devices are free to communicate directly with each other
  but they still must associate with the PAN coordinator before they can participate in peer-to-peer communication
Data transfer between the device and its PAN coordinator is always initiated by the device
  allows a device to determine when data is transferred and to maximize its energy savings
    when a device wants to send data to the PAN coordinator, it can use the previously described channel access method
    the PAN coordinator transmits data intended for a device only after the device explicitly requested such a transmission
  in both cases, optional acknowledgments can be used to let the PAN coordinator or device know that the transmission was successful

## Slide 186: IEEE 802.15.4 and ZigBee
Challenges:
  standard does not clearly define the operation of the peer-to-peer approach
  in large WSNs, it is unlikely that all devices will be able to use the same PAN coordinator
  standard does allow communication among PAN coordinators, but this again is not well defined

## Slide 187: Outline
Wireless MAC protocols
Characteristics of MAC Protocols in Sensor Networks
Contention-Free MAC Protocols
Contention-Based MAC Protocols
Hybrid MAC Protocols

## Slide 188: Characteristics of MAC Protocols in WSN
Most MAC protocols are built for fairness
  everybody should get an equal amount of resources
  no one should receive special treatment
In a WSN, all nodes cooperate to achieve a common purpose, therefore fairness is less of a concern
Instead, wireless nodes are mostly concerned with energy consumption
Sensing applications may value low latency or high reliability over fairness

## Slide 189: Energy Efficiency
Sensor nodes must operate using finite energy sources, therefore MAC protocols must consider energy efficiency
Common technique: dynamic power management (DPM)
  a resource can be moved between different operational modes (active, idle, and asleep)
  for resources such as the network, the active mode can group together multiple different modes of activity, e.g., transmitting and receiving
Periodic traffic models are very common in WSNs
  significant energy savings can be obtained by putting a device into a low-power sleep mode
  fraction of time a sensor nodes spends in active mode is called the duty cycle
    often very small due to infrequent and brief data transmissions occurring in most sensor networks

## Slide 190: Energy Efficiency

## Slide 191: Energy Efficiency
Reasons for energy inefficiency
  idle listening
  inefficient protocol designs (e.g., large packet headers)
  reliability features (collisions requiring retransmissions or other error control mechanisms)
  control messages to address the hidden-terminal problem
  choice of modulation scheme
  choice of transmission rate
  overemitting

## Slide 192: Scalability
Many wireless MAC protocols have been designed for use in infrastructure-based networks
  access points or controller nodes arbitrate access to the channel and perform some centralized coordination and management functions
Most wireless sensor networks rely on multi-hop and peer-to-peer communications without centralized coordinators
MAC protocols must be able to allow for efficient use of resources without incurring unacceptable overheads, particularly in very large networks

## Slide 193: Scalability
MAC protocols based on CDMA have to cache a large number of code (may be impractical for resource-constrained sensor devices)
WSNs are not only constrained in their energy resources, but also in their processing and memory capacities
MAC protocols should not impose excessive computational burden should not require too much memory to save state information

## Slide 194: Adaptability
A key characteristic of a WSN is its ability to self-manage
  adapt to changes in the network
  including changes in topology, network size, density, and traffic characteristics
A MAC protocol for a WSN should be able to gracefully adapt to such changes without significant overheads
This requirement generally favors protocols that are dynamic in nature
  protocols that make medium access decisions based on current demand and network state
Protocols with fixed assignments (e.g., TDMA with fixed-size frames and slots) may incur large overheads due to adaptations of such assignments that may affect many or all nodes in the network

## Slide 195: Low Latency and Predictability
Many WSN applications have timeliness requirements
  sensor data must be collected, aggregated, and delivered within certain latency constraints or deadlines
  example: wildfire detection (sensor data must be delivered to monitoring stations in a timely fashion to ensure timely responses)
MAC protocol design
  choice of frame size and slot allocations in TDMA-based protocols lead to large delays
  in contention-based protocols, nodes may be able to access the wireless medium sooner (than TDMA), but collisions and the resulting retransmissions incur delays
  choice of MAC protocol can affect how predictable the experienced delay is (expressed as upper latency bounds )
  some contention-based MAC protocols allow the theoretical possibility of starvation

## Slide 196: Reliability
Common requirement for WSNs
MAC protocol design affects reliability
  responsible for detecting and recovering from transmission errors and collisions

## Slide 197: Outline
Wireless MAC protocols
Characteristics of MAC Protocols in Sensor Networks
Contention-Free MAC Protocols
Contention-Based MAC Protocols
Hybrid MAC Protocols

## Slide 198: Contention-Free MAC Protocols
Concept:
  allow only one sensor node to access the channel at any given time
  assuming a perfect medium and environment
    i.e., no other competing networks or misbehaving devices exist that could otherwise cause collisions or even jam a channel
Contention-free protocols allocate resources to individual nodes to ensure exclusive resource access by only one node at any given time
Exposes a number of characteristics
  node knows exactly when it has to turn on its radio
  during all other times, radio can be turned off to preserve energy
  fixed slot allocations impose upper bounds on delay
  difficult to design schedules for large networks
  difficult to handle changes in topology, density, traffic load

## Slide 199: Traffic-Adaptive Medium Access
TRAMA is an example of a contention-free MAC protocol with the goal to increase network throughput and energy efficiency (compared to TDMA)
It uses a distributed election scheme to determine when nodes are allowed to transmit
  based on information about the traffic at each node
  avoids assigning slots to nodes with no traffic to send (increased throughput)
  allows nodes to determine when they can become idle and do not have to listen to the channel (increased energy efficiency)
TRAMA assumes a time-slotted channel, where time is dived into:
  periodic random-access intervals (signaling slots)
  scheduled-access intervals (transmission slots)

## Slide 200: Traffic-Adaptive Medium Access
Random-access intervals
  Neighbor Protocol (NP) is used to propagate one-hop neighbor information among neighboring nodes
    nodes join a network by transmitting during a randomly selected slot
    packets transmitted during these slots are used to gather neighborhood information by carrying a set of added and deleted neighbors
    in case no changes have occurred, these packets serve as “keep-alive” beacons
  NP allows nodes to obtain consistent two-hop topology information

## Slide 201: Traffic-Adaptive Medium Access
Random-access intervals (contd.)
  Schedule Exchange Protocol (SEP) establishes and broadcasts actual schedules (i.e., allocations of slots to a node)
    each node computes a duration SCHEDULE_INTERVAL
      – represents the number of slots for which the node can announce its schedule to its neighbors
      – this duration depends on the rate at which the node ʼ s applications can produce packets
    at time t, the node then computes the number of slots within [t, t+ SCHEDULE_INTERVAL] for which it has the highest priority among its two-hop neighbors
    the node announces the selected slots and the intended receivers using a schedule packet
    the last slot in this schedule is used to announce the next schedule for the next interval

## Slide 202: Traffic-Adaptive Medium Access
Random-access intervals (contd.)
  Schedule Exchange Protocol (SEP) (contd.)
    example:
      – a nodeʼ s SCHEDULE_INTERVAL is 100 slots
      – the current time (slot number) is 1000
      – a possible slot selection for interval [1000, 1100] for this node could be 1011, 1021, 1049, 1050, and 1093
      – during slot 1093, the node broadcasts its new schedule for interval [1093, 1193]
    list of intended receivers in the schedule packet is implemented as a bitmap
      – length of a bitmap is equal to the number of one-hop neighbors
      each bit in the bitmap corresponds to one particular receiver ordered by its identities
      every node can determine the receiver address based on the bitmap and its list of neighbors

## Slide 203: Traffic-Adaptive Medium Access
Random-access intervals (contd.)
  Schedule Exchange Protocol (SEP) (contd.)
    slot selection is based on the nodeʼ s priority at time t
      – uses a pseudo-random hash of the concatenation of the nodeʼ s identity i and t :
      – node can indicate which slots it gives up, allowing other nodes to claim these unused slots
    a node can determine its state for any given time slot t based on its two-hop neighborhood information and the announced schedules
      – node i is in the transmit (TX) state if it has the highest priority and if it has data to send
      – node i is in the receive (RX) state if it is the intended receiver of the transmitter during slot t
      – otherwise, the node can be switched into the sleep (SL) state

## Slide 204: Traffic-Adaptive Medium Access
Summary
  compared to CSMA-based protocols
    reduces the probability of collisions
    increases the sleep time and energy savings
  unlike standard TDMA approaches
    TRAMA divides time into random-access and scheduled-access intervals
    during the random-access intervals
      – nodes are awake to either transmit or receive topology information
      – the length of the random-access interval affects the overall duty cycle and achievable energy savings of a node

## Slide 205: Low-Energy Adaptive Clustering Hierarchy
The LEACH protocol combines TDMA-style contention-free communication with a clustering algorithm for wireless sensor networks
  a cluster consists of a single cluster head and any number of cluster members, which only communicate with their cluster head
  clustering is a popular approach for sensor networks
    facilitates data aggregation and in-network processing at the cluster head
    reduces the amount of data that needs to be transmitted to the base station
LEACH operates in rounds consisting of two phases:
  A setup phase
  A steady-state phase

## Slide 206: Low-Energy Adaptive Clustering Hierarchy
Setup phase
  cluster heads are determined and communication schedules within each cluster are established
  since the cluster head is responsible for coordinating cluster activity and forwarding data to the base station, its energy requirements will be significantly larger compared to other sensor nodes
  therefore, LEACH rotates the cluster head responsibility among sensor nodes to evenly distribute the energy load
    every sensor i elects itself to be a cluster head with a certain probability Pi(t)
    In a network with N nodes and a desired number of cluster heads of k, the probabilities can be chosen to satisfy:
    =k

## Slide 207: Low-Energy Adaptive Clustering Hierarchy
There are various approaches to choose Pi (t) , e.g.,:
This approach uses an indicator function Ci (t) to determine whether node i has been a cluster head in the r mod (N/k) previous rounds
Only nodes that have not been cluster heads recently are candidates for the cluster head role, in order to evenly distribute the cluster head responsibility (and energy overhead) among all nodes

## Slide 208: Low-Energy Adaptive Clustering Hierarchy
This approach does not consider the actual amount of energy available to each node
An alternative approach to determining the probability of becoming a cluster head can be used:
  Ei(t) is node i ʼ s actual current energy and Etotal(t) is the sum of the energy levels of all nodes
  a disadvantage of this approach is that every node must know (or estimate) Etotal(t)

## Slide 209: Low-Energy Adaptive Clustering Hierarchy
Once a sensor node has determined that it will serve as cluster head for the next round, it informs other sensor nodes of its new role by broadcasting an advertisement message (ADV) using a non-persistent CSMA protocol
Every sensor node joins a cluster by selecting the cluster head that can be reached with the smallest amount of transmit energy, based on received signal strength of the ADV messages from the cluster heads
Joining is achieved by transmitting a join-request (Join-REQ) message to the chosen cluster head using CSMA
The cluster head establishes a transmission schedule for its cluster and transmits this schedule to each node in its cluster

## Slide 210: Low-Energy Adaptive Clustering Hierarchy
Steady-state phase
  a sensor node communicates only with the cluster head
    it is allowed to transmit data only during its allocated slots (indicated by the schedule received from the cluster head)
  the responsibility of the cluster head is to forward sensor data originating at one of its sensor nodes to the base station
  in order to preserve energy
    each cluster member uses the minimum required transmit power to reach the cluster head
    each cluster member turns off the wireless radio between its designated slots
  the cluster head remains awake at all times
    to receive sensor data from its cluster members
    to communicate with the base station

## Slide 211: Low-Energy Adaptive Clustering Hierarchy
Sensor nodes use the direct sequence spread spectrum (DSSS) 直接序列扩频technique to limit the interference among clusters, while intra-cluster communication is contention-free using TDMA-style frames and slots
Communication occurring in one cluster can still interfere with communication in another cluster
Each cluster uses a spreading sequence that is different from the spreading sequences used in neighboring clusters
Another reserved sequence is used for communication between cluster heads and the base station
Communication between cluster heads and base station is based on CSMA
Before a cluster head transmits data, it first senses the channel to see if there is an ongoing transmission using the same spreading code

## Slide 212: Low-Energy Adaptive Clustering Hierarchy
LEACH-C
  variation of LEACH protocol
  relies on the base station to determine the cluster heads
    during setup phase, each sensor node transmits its location and energy levels to the base station
    based on this information, the base station determines the cluster heads and informs the cluster heads of their new role
    other sensor nodes can then join clusters using join messages as described in the original LEACH protocol

## Slide 213: Low-Energy Adaptive Clustering Hierarchy
Summary
  LEACH relies on a variety of techniques to reduce energy consumption
    minimum transmit energy
    avoiding idle listening of cluster members
  LEACH attempts to obtain contention-free communication
    schedule-based communication
    DSSS
  intra-cluster communication is contention-free and interferences among clusters are avoided
  communication between the cluster heads and the base station is still based on CSMA
  assumes that all nodes are able to reach the base station (affects the scalability of this protocol; can be addressed using multi-hop routing or by implementing a hierarchical clustering approach)

## Slide 214: Y-MAC
Y-MAC uses TDMA-based medium access but for multiple channels
Divides time into frames and slots
  each frame contains a broadcast period and a unicast period
  every node must wake up at the beginning of a broadcast period
  nodes contend for access to the medium during this period
    if there are no incoming broadcast messages, each node turns off its radio awaiting its first assigned slot in the unicast period
    each slot in the unicast period is assigned to only one node for receiving data

## Slide 215: Y-MAC
Y-MAC uses a receiver-driven model
  can be more energy-efficient under light traffic conditions, because each node samples the medium only in its own receive time slots
  particularly important for radio transceivers, where the energy costs for receiving are greater than for transmitting (e.g., due to sophisticated despreading (解扩) and error correction techniques)
Medium access in Y-MAC is based on synchronous low power listening

## Slide 216: Y-MAC
The contention window (at beginning of each slot) resolves contention between multiple senders
  a node wishing to send data sets a random wait time (back-off value) within the contention window
  after this wait time, the node wakes up and senses the medium for activity for a certain amount of time
    if the medium is free, the node sends a preamble until the end of the contention window to suppress competing transmissions and the receiver wakes up at the end of the contention window to wait for packets in its assigned slot
    if the medium receives no signal from any of its neighboring nodes, it turns off the radio and returns to the sleep mode

## Slide 217: Y-MAC
Unicast period
  messages are initially exchanged on the base channel
  at the beginning of its receive slot
    a receiver switches its frequency to the base channel
    the node that won the medium in the contention window also uses the base channel to transmit its packet
    the receiver acknowledges this packet (if the acknowledgment request flag was set in the packet)
Broadcast period
  every node tunes to the base channel
  the potential senders take part in the contention process described above

## Slide 218: Y-MAC
Every node polls the medium only during broadcast time slots and its own unicast receive time slots
  makes this approach energy-efficient
  under heavy traffic conditions, many unicast messages may have to wait in the message queue or are dropped due to the limited bandwidth reserved for the receiving node
  as a consequence, Y-MAC uses a channel hopping mechanism to reduce packet delivery latency

## Slide 219: Y-MAC
After receiving a packet during its time slot on the base channel, the receiving node hops to the next channel and sends a notification
  it can continue to receive packets on the second channel
  contention for the medium in the second channel is resolved as before
At the end of this slot, the receiving node can decide to hop again to another channel
  until reaching the last channel or
  until no more data is being received
The hopping sequence generation algorithm
  determines the actual hopping sequence among the available channels
  should guarantee that there is only one receiver among one-hop neighbors on any particular channel

## Slide 220: Y-MAC
Summary
  Y-MAC uses slot assignments (such as TDMA)
  communication is receiver-driven to ensure low-energy consumption
    i.e., a receiver briefly samples the medium during its slot and returns to the sleep mode if no packets arrive
  uses multiple channels
    to increase the achievable throughput
    to reduce delivery latency
  main drawbacks of the Y-MAC approach:
    has the same flexibility and scalability issues as TDMA (i.e., fixed slot allocations)
    requires sensor nodes with multiple radio channels

## Slide 221: Lightweight Medium Access Control
The LMAC protocol is based on TDMA
  each slot is owned by exactly one node
  nodes execute a distributed algorithm to allocate slots instead of relying on a central manager to assign slots to nodes
  each node uses its slots to transmit a message consisting of two parts:
    control message
      – identity of the time slot controller
      – distance (in hops) of the node to the gateway (base station)
      – address of the intended receiver
      – length of the data unit
    data unit
  upon receiving a control message, a node determines if it is the intended receiver and decides whether to stay awake or to turn off the radio until the next slot

## Slide 222: Lightweight Medium Access Control

## Slide 223: Lightweight Medium Access Control
The Occupied Slots field of the control message is a bit-mask of slots
  where an unoccupied slot is represented by 0
  an occupied slot is represented by 1
A node is able to determine unoccupied slots by combining control messages from all neighbors
The process of claiming slots starts at the gateway device , which determines its own slots
After one frame, all direct neighbors of the gateway know the gateway ʼ s slots and choose their own slots

## Slide 224: Lightweight Medium Access Control
This process continues throughout the network and during each frame, a new set of nodes with a higher hop distance from the gateway determine their slots
Each node must select slots that are not in use within a two-hop neighborhood
Slots are selected randomly, so it is possible for multiple nodes to select the same slot
  will result in a collision of control messages during the slot
  can be observed by the competing nodes, therefore, they will restart the slot selection process

## Slide 225: Mobile LMAC
Slot allocations in LMAC are computed only once, therefore, this protocol is not suitable for mobile sensor network, where nodes frequently join and leave other nodes ʼ radio ranges
Mobile LMAC (MLMAC) uses a distributed slot allocation mechanism, but it is able to adapt to changes in the network topology
  When a node X leaves the radio range of node Y, both nodes will realize that they no longer receive control messages from each other and they will remove each other from their neighbor lists
  Assume that node X moves into the radio range of node Z and that another node in Z ʼs range, node W, uses the same slot as X
  Control messages from X and W will collide at Z and node Z will no longer receive any correct control messages during this slot and will therefore mark this slot as unused
  Nodes X and W will receive Zʼ s control message, indicating that their slot is unused and meaning that there must have been a collision.
  As a consequence, they give up their current slot and restart the slot selection mechanism

## Slide 226: LMAC and MLMAC
Both LMAC and MLMAC have the same advantages as TDMA
  collision-free communication
  energy efficiency
Additionally, they are able to establish transmission schedules in a distributed fashion
However, in both protocols
  slot size is fixed
  slot allocations are also fixed
    except when a node has to restart the slot selection mechanism
  leading to bandwidth inefficiency

## Slide 227: Contention-Based MAC Protocols
The main advantage is simplicity compared to most schedule-based techniques
  schedule-based MAC protocols must save and maintain schedules or tables indicating the transmission order
  most contention-based protocols do not require to save, maintain, or share state information
  this also allows contention-based protocols to adapt quickly to changes in network topologies or traffic characteristics
However, they typically result in higher collision rates and overheads due to idle listening and overhearing (overheads usually refer to additional bits in a packet or additional packets such as control packets)
They may also suffer from fairness issues (i.e., some nodes may be able to obtain more frequent channel accesses than others)

## Slide 228: Power Aware Multi-Access with Signaling
The PAMAS protocol attempts to avoid unnecessary energy expenditure caused by overhearing
PAMAS uses two separate channels to prevent collisions among data transmissions: one for data frames and one for control frames (ready-to-send or RTS and clear-to-send or CTS)
The separate signaling channel allows nodes to determine when and how long to power down their wireless transceivers
  devices transmit busy tones on the control channel to ensure that devices that did not overhear either RTS or CTS will not access the data channel for transmissions

## Slide 229: Power Aware Multi-Access with Signaling
Initiating a data transfer
  a PAMAS device sends an RTS message over the control channel to the receiver
  receiver responds with CTS if it does not detect activity on the data channel and has not overheard other recent RTS or CTS messages
  if the source does not receive a CTS within a specific timeout interval, it will attempt to transmit again after a back-off time (exponential back-off algorithm)
  otherwise, it begins data transmission and the receiver node issues a busy tone over the control channel (whose length is greater than twice the length of a CTS)
  the receiver device also issues a busy tone over the control channel whenever it receives an RTS message or detects noise on the control channel while it receives a frame
    done to corrupt possible CTS message replies to the detected RTS, thereby blocking any data transmission of the receiverʼs neighbors

## Slide 230: Power Aware Multi-Access with Signaling
Every node in a PAMAS network independently decides when to power off its transceiver
Specifically, a node decides to turn off its transceiver whenever one of two conditions holds:
  a neighbor begins a transmission and the node has no frames to transmit
  a neighbor transmits a frame to another neighbor, even if the node has frames to transmit
A node can easily detect either condition by
  overhearing its neighborʼ s transmissions (condition 1) or
  overhearing its neighborʼ s busy tone (condition 2)
A node can identify how long to power down its transceiver by embedding the size or expected transmission duration into messages

## Slide 231: Power Aware Multi-Access with Signaling
However, when a transmission begins while a node is still asleep, it does not know how long this transmission will last and how long it should continue to sleep
Therefore, the node issues a probe frame (containing a certain time interval) over the control channel to all transmitting nodes in its neighborhood
  all transmitters that will complete during this interval respond with their predicted completion time
  if such a response is received by the awakening node without collision, it can return to the sleep mode until the completion time indicated by the transmitting node
  if multiple transmitters respond and their responses collide, the node reissues the probe frame with a shorter time interval
  similarly, if the node did not receive a response, it can reissue the probe with a different time interval
  in effect, the node chooses time intervals to perform a binary search to identify when the last ongoing transmission will end

## Slide 232: Sensor MAC
The goal of the S-MAC protocol is
  to reduce unnecessary energy consumption
  while providing good scalability and collision avoidance mechanism
S-MAC adopts a duty-cycle approach
  nodes periodically transition between a listen state and a sleep state
  each node chooses its own schedule, although it is preferred when nodes synchronize their schedules such that nodes listen or sleep at the same time
  nodes using the same schedule are considered to belong to the same virtual cluster (but no real clustering takes place)
    all nodes are free to communicate with nodes outside their clusters

## Slide 233: Sensor MAC
Nodes periodically exchange their schedules with their neighbors using SYNC messages (every node knows when any of its neighbors will be awake)
If node A wants to communicate with a neighbor B that uses a different schedule, A simply waits until B is listening and then initiates the data transfer
  contention for the medium is resolved using the RTS/CTS scheme
In order to choose a schedule, a node initially listens to the medium for a certain amount of time
  if this node receives a schedule from a neighbor, it chooses this schedule as its own and this node becomes a follower
  the node broadcasts its new schedule after a random delay td to minimize the possibility for collisions from multiple new followers

## Slide 234: Sensor MAC
Nodes can adopt multiple schedules if a node receives a different schedule after it has broadcast its own schedule
  it then adopts both schedules
If a node does not hear a schedule from another node
  it determines its own schedule
  broadcasts this schedule to any potential neighbors
  and this node becomes a synchronizer (in that other nodes will begin to synchronize themselves with it)

## Slide 235: Sensor MAC
S-MAC divides a node ʼ s listen interval further into
  a part for receiving SYNC packets
  a part for receiving RTS messages
Each part is further divided into small slots to facilitate carrier sensing

## Slide 236: Sensor MAC
A node trying to send a SYNC or RTS message randomly selects a time slot within the SYNC or RTS part of the interval, respectively
  senses the carrier for activity from when the receiver begins listening to the selected slot
  if no activity has been detected, it wins the medium and begins transmission
Contention for the medium is addressed using collision avoidance based on RTS/CTS handshakes (S-MAC adopts a contention-based approach)
  when a node hears an RTS or CTS and concludes that it cannot transmit or receive at the same time, it can go to sleep to avoid wasting energy caused by overhearing

## Slide 237: Sensor MAC
Summary
  S-MAC is a contention-based protocol
  utilizes the sleep mode of wireless radios to trade energy for throughput and latency
  collision avoidance is based on RTS/CTS (which is not used by broadcast packets, thereby increasing the collision probability)
  duty cycle parameters (sleep and listen periods) are decided beforehand and may be inefficient for the actual traffic characteristics in the network

## Slide 238: Timeout MAC
If there is little traffic, S-MAC can actually waste energy because the listening period of S-MAC is of fixed duration; If traffic is heavy, fixed duration may not be large enough
Therefore, the T-MAC protocol is a variation of S-MAC that uses an active period that adapts to traffic density
Nodes wake up during the beginning of a slot to listen very briefly for activity and return to the sleep mode when no communication has been observed
When a node transmits, receives, or overhears a message, it remains awake for a brief period of time after completion of the message transfer to see if more traffic can be observed
  this brief timeout interval allows a node to return to the sleep mode as quickly as possible
  the end effect is that a node ʼ s awake times will increase with the heavier traffic and will be very brief if traffic is light

## Slide 239: Timeout MAC
To reduce potential collisions, each node waits for a random period of time within a fixed contention interval before the medium is accessed

## Slide 240: Timeout MAC
Once a node hears a CTS, it knows that another node won the medium
This node then stays awake until the end of the transmission, which can be observed by overhearing the acknowledgment (ACK) sent by node B
This event initiates the beginning of the next contention interval and node C will have an opportunity to transmit its data if it wins the medium
In figure, assume that messages flow from top to bottom
  node A sends only to node B, node B sends to node C
  every time node C wants to send a message to node D, C must contend for the medium
    C may lose to node B (B may transmit an RTS before C does) or
    C may lose to node A (C overhears a CTS transmitted by node B)
  while node C stays awake after overhearing node B ʼ s CTS message, its intended receiver (node D) is not aware of C ʼ s intention to transmit data and therefore returns to the sleep mode after TA has expired

## Slide 241: Timeout MAC
Early sleeping problem
  possible solution: future-request-to-send technique
    a node with pending data can inform its intended receiver by transmitting a future-request-to-send (FRTS) packet immediately after overhearing a CTS message
    node D, upon receiving the FRTS message, knows that node C will attempt to send data to it and will therefore remain active
    however, sending an FRTS message immediately after CTS could interfere with node Bʼs reception of node Aʼs data
    therefore, Node A first sends a dummy message called Data-Send (DS) to delay the transmission of the actual data
      DS has the same size as FRTS
      DS can collide with FRTS at node B, which is of no consequence since it does not contain any useful information

## Slide 242: Timeout MAC
Summary
  T-MACʼs adaptive approach allows it to adjust a nodeʼ s sleep and awake intervals based on the traffic load
  nodes send messages as bursts of variable length and sleep between such bursts to conserve energy
  both S-MAC and T-MAC concentrate message exchanges to small periods of time, resulting in inefficiencies under high traffic loads
  intended receivers are kept awake using messages that indicate future transmissions, which can significantly increase the idle listening times (and energy consumption) of nodes

## Slide 243: Routing-Enhanced MAC
The RMAC protocol is another example of a protocol that exploits duty cycles to preserve energy
Compared to S-MAC, it attempts to improve upon end-to-end latency and contention avoidance
They key idea behind RMAC is to align the sleep/wake periods of nodes along the path of sensor data such that a packet can be forwarded to the destination within a single operational cycle
It achieves this by sending a control frame along the route to inform nodes of the upcoming packet, allowing them to learn when to be awake to receive and forward this packet

## Slide 244: Routing-Enhanced MAC
RMAC partitions an operational cycle into three components:
  SYNC period
    nodes synchronize their clocks (to maintain sufficient precision)
  DATA period
    used to announce and initiate the packet transmission process along packetʼs route to destination
    contention-based
      sender waits for a randomly chosen period of time plus an additional DIFS period (and senses the medium during this time)
      if no activity is detected, the sender transmits a Pioneer Control Frame (PION) containing the addresses of the sender, destination, and next hop, the duration of the transmission, and the number of hops travelled so far (0 at sender)
      the next hop along the route looks up the next hop for this route and forwards the PION to the next hop after waiting for a SIFS period
      this process continues until the PION reaches the destination
  SLEEP period

## Slide 245: Routing-Enhanced MAC

## Slide 246: Routing-Enhanced MAC
Actual data transmission takes place during the SLEEP period
Example in figure:
  node A stays awake to receive the data packet from the sender and after successful transmission A returns an acknowledgment (ACK)
  all data and ACK packets are separated by a SIFS period similar to the PION schedule during the DATA period
  after receiving the ACK from node A, the sender has completed its part and it can return its radio into the sleep mode
  node A relays the received packet to the next hop (node B) and also returns its radio to sleep mode once B has acknowledged the data packet
  this process continues until the data packet has been received and acknowledged by the destination

## Slide 247: Routing-Enhanced MAC
The sender and node A stay awake after the DATA period to immediately begin the transmission of the data packet over the first hop
All other nodes along the route can turn off their radios after the DATA period has completed to further preserve energy
Each node wakes up at the right time to receive the data packet from the upstream node
This time to wake up can be computed by node i as:
  where size(DATA) and size(ACK) are the times required to send a single data and ACK frame

## Slide 248: Routing-Enhanced MAC
Summary
  RMAC addresses the large latencies often experienced in MAC protocols based on duty cycles
  it is able to perform end-to-end packet delivery within a single operational cycle
  it also alleviates contention by separating medium contention and data transfer into two separate periods
  however, collisions can still occur, even on the data packets during the SLEEP period
    a source always commences transmission at the beginning of the SLEEP period, therefore it is possible that data packets coming from two different sources (which succeeded in the PION scheduling process during the DATA period, but cannot see each other) may still collide

## Slide 249: Routing-Enhanced MAC
This problem has been addressed by a similar protocol called Demand-Wakeup (DW-MAC)
  the schedule is a one-to-one mapping between a DATA period and the following SLEEP period:
    TiS is the start time of the scheduling frame (SCH) (the equivalent of the pioneer frame in RMAC) measured from the start of the DATA period
    TiD is the start time of the data transmission in the SLEEP period (measured from the start of the SLEEP period)
    Tsleep and Tdata are the durations of the SLEEP and DATA periods
  data packet transmissions do not necessarily coincide with the start of the SLEEP period, but instead depend on the contention window during the DATA period
    reduces the risk of collisions during the SLEEP period

## Slide 250: Data-Gathering MAC
The DMAC protocol exploits the fact that many wireless sensor networks rely on convergecast as communication pattern, i.e., data from sensor nodes are collected at a central node (the “sink”) in a data-gathering tree
The goal of DMAC is to deliver data along the data gathering tree with low latency and high energy efficiency
The duty cycles of nodes along the multi-hop path to the sink are “staggered”, i.e., nodes wake up sequentially like a chain reaction

## Slide 251: Data-Gathering MAC
Nodes switch between sending, receiving, and sleep states
During the sending state, a node sends a packet to the next hop node on the route and awaits an acknowledgment (ACK)
At the same time, the next hop node is in the receiving state, immediately followed by a sending state to forward the packet to the next hop (unless the node is the destination of packet)
A node enters the sleep state between these intervals of receiving and sending of packets, where it can power down its radio to preserve energy
The sending and receiving intervals are large enough for exactly one packet
Since there are no queuing delays, a node at depth d in the tree can then deliver a packet to the sink within d intervals
While limiting a nodeʼ s activity to brief intervals for sending and receiving reduces the contention, collisions can still occur
  e.g., nodes with the same depth in the tree will have synchronized schedules

## Slide 252: Data-Gathering MAC
If a sender does not receive an ACK, it queues the packet until the next sending interval and after three failed retransmissions, the packet will be dropped
To reduce collisions, nodes do not transmit immediately at the beginning of the sending slot, but instead have a back-off period (BP) plus a random time within a contention window
When a node has multiple packets to send during a sending slot!
  it can increase its own duty cycle and
  it requests other nodes along the route to the sink to do the same !
This is implemented through a slot-by-slot renewal mechanism using a more data flag in the MAC header
A receiver checks for this flag and if set
  it returns an acknowledgment that has also the more data flag set
  it then stays awake to receive and forward one additional packet

## Slide 253: Data-Gathering MAC
Summary
  DMAC ʼ s staggering technique achieves very low latency
  nodes only stay awake for brief receive and send intervals
  since many nodes in the data-gathering tree share the same schedule, collisions will occur and DMAC only employs limited collision avoidance methods
  DMAC works best for networks in which the transmission paths and rates are well known and do not change over time

## Slide 254: Hybrid MAC Protocols
Display characteristics of both categories
  attempt to reduce the number of collisions by relying on features present in contention-free medium access protocols
  take advantage of the flexibility and low complexity of contention-based protocols

## Slide 255: Zebra MAC
The Z-MAC protocol uses frames and slots to provide contention-free access to the wireless medium
  similar to TDMA-based protocols
However, Z-MAC also allows nodes to utilize slots they do not own using CSMA with prioritized back-off times
As a consequence:
  in low-traffic scenarios, Z-MAC emulates a CSMA-based approach
  when traffic loads are high, Z-MAC emulates a TDMA-based approach

## Slide 256: Zebra MAC
When a node starts up, it enters a setup phase to allow it
  to discover its neighbors
  to obtain its slot in the TDMA frame
Every node periodically broadcasts a message containing a list of its neighbors
  through this process, a node learns about its 1-hop and 2-hop neighbors
  this information is used as input to a distributed slot assignment protocol (provides each node with time slots)
  ensures a schedule where no two nodes within an 2-hop neighborhood will be assigned the same slot

## Slide 257: Zebra MAC
Z-MAC allows nodes to select the periodicity of their assigned slots where different nodes can have different periods (time frames or TF)
The advantage of this approach is that it is not necessary to propagate a maximum slot number (MSN) to the entire network
The protocol can adapt slot allocations locally
  assume that node i is assigned slot si
  and Fi represents the MSN within the nodeʼs 2-hop neighborhood
  then: i ʼs TF is set to be 2a
    a is a positive integer that satisfies 2a-1≤Fi<2a-1
  node i then uses the si th slot in every 2a time frame

## Slide 258: Zebra MAC
Example with eight nodes
  number indicates the assigned slot for each node
  number in parenthesis is Fi
  bottom part of the figure shows the corresponding schedule for all nodes
    light-shaded slots are the ones used for transmissions
    dark-shaded slots are the empty slots that are not used by any 1-hop or 2-hop neighbors
  if a global time frame is used, the chosen time frame size will be 6
    nodes A and B will be allowed to use their slots only once every 6 slots even though their frame sizes are 2 each

## Slide 259: Zebra MAC
In Z-MAC, these nodes can use frame size 4
  increases the concurrency in the channel usage
  reduces message delays
The resulting schedule shows that some slots are not assigned to any node
  specifically slots 6 and 7
In a global time frame, a frame size could have been chosen that reduces the number of empty slots
However, Z-MAC allows nodes to compete for these “extra” slots using CSMA

## Slide 260: Zebra MAC
After the schedule has been determined, every node forwards its frame size and slot number to its 1-hop and 2-hop neighbors
Even though slots are owned by nodes, Z-MAC uses CSMA to determine who may transmit
However, slot owners are given preference
  by using a random back-off value chosen from the range [0, To]
  whereas other nodes choose their back-off values from the range [To, Tno]

## Slide 261: Zebra MAC
Z-MAC also uses explicit contention notification (ECN) to which it has a message
  where each node decides to whether to send an ECN message to a neighbor based on its local estimate of the contention level (e.g., determined using the packet loss rate or channel noise level)
  this neighbor then broadcasts the ECN to its own neighbors, which then enter a high contention level (HCL) mode
  a node in the HCL mode only transmits data in its own slots or slots belonging to its 1-hop neighbors
    thereby reducing the contention between 2-hop neighbors
it returns to a low contention level (LCL) mode if it has not received any ECN messages for a certain amount of time

## Slide 262: Zebra MAC
Summary
  Z-MAC adopts characteristics found in both TDMA and CSMA protocols
  allowing it to quickly adapt to changing traffic conditions
  under light traffic loads Z-MAC behaves more like CSMA
  under heavy traffic loads contention for slots is reduced
  Z-MAC requires an explicit setup phase (consumes both time and energy)
  while ECN messages be used to reduce the contention locally
    these messages add more traffic to an already busy network and take time to propagate
    thereby causing delays in the adaptation to a more TDMA-like behavior

## Slide 263: Summary
The choice of a medium access protocol has a substantial impact on the performance and energy-efficiency of a WSN
MAC protocols should also be designed to accommodate changes in network topology and traffic characteristics
Latency, throughput, and fairness among competing nodes determined or affected by the characteristics of the MAC layer
Protocols based on transmission schedules
  collision-free
  resource-inefficient
  may require well synchronized nodes throughout the network
  difficult to adapt to changing topologies

## Slide 264: Summary
Protocols that let nodes compete for access to the medium
more flexible (easily accommodate changing network topologies)
require less overhead
not collision-free
must possess features that allow them to recover from collisions
network utilization may suffer when collisions occur frequently

## Slide 265: Chapter 6 Network Layer

## Slide 266: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 267: Network Layer Responsibility
Direct communication model: every sensors communicates directly (single-hop) with the sink device (base station)
  not feasible due to lack of energy, scale of network, lack of unobstructed communication links between sensors and sink
Multi-hop communication model: sensors cooperate in propagating sensor data towards the sink
Routing is a key responsibility of the network layer
Routing protocol is responsible for finding and maintaining path from sensor to sink

## Slide 268: Classification of Routing Protocols

## Slide 269: Classification of Routing Protocols
Network organization
  flat: all nodes are “equal”
  hierarchical: different “roles” for different nodes (e.g., cluster heads versus cluster members)
  location-based: nodes rely on location information
Route discovery
  reactive (on-demand): find route only when needed
  proactive (table-driven): establish routes before they are needed
  hybrid: protocols with reactive and proactive characteristics
Protocol operation
  negotiation-based: negotiate data transfers before they occur
  multi-path: use multiple routes simultaneously
  query-based: receiver-initiated
  QoS-based: satisfy certain QoS (Quality-of-Service) constraints
  coherent-based: perform only minimum amount of in-network processing

## Slide 270: Routing Metrics
Minimum hop (shortest hop)
Energy
  minimum energy consumed per packet
  maximum time to network partition
  minimize variance in node power levels
  maximum (average) energy capacity
  maximum minimum energy capacity
Quality-of-Service
  latency (delay), throughput, jitter, packet loss, error rate
Robustness
  link quality, link stability

## Slide 271: Routing Metrics (Example)
Numbers along links: cost for transmission
Numbers in parentheses: remaining energy capacity

## Slide 272: New Arch.
Van Jacobson：primary contributors to the TCP/IP protocol stack
Networking Named Content，CoNEXT’09

## Slide 273: New Arch.
Directed Diffusion
Date-centric Routing
“Van Jaobson suggested some of the initial ideas that later led to the design of direted diffusion.”
Deborah Estrin

## Slide 274: Evolution of Communication Abstraction

## Slide 275: Flooding
flooding faces three more challenges:
  Implosion: nodes will re-broadcast even when neighbors already have a copy
  Overlap: sensor data contains redundant information
  Resource blindness: resource constraints are ignored
Every sensor node (re-)broadcasts sensor data to all of its neighbors
Simple and reliable technique
Incurs large traffic overhead (maximum-hop counts and sequence numbers can be used to limit broadcasts and eliminate duplicates)

## Slide 276: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 277: SPIN Family of Protocols
Sensor Protocols for Information via Negotiation (SPIN)
Example of data-centric routing
Uses negotiations to address all problems of flooding
  implosion: nodes negotiate before data transmission
  overlap: nodes negotiate before data transmission
  resource blindness: resource manager keeps track of actual resource consumption and adapts routing and communication behavior
SPIN uses meta-data to succinctly and completely describe sensor data
Requirements:
  if x describes the meta-data for some sensor data X, the size of x (in bytes) must be less than the size of X
  if two pieces of sensor data differ, their meta-data representations should differ too

## Slide 278: SPIN-PP
Optimized for networks using point-to-point transmission media (two nodes communicate exclusively with each other without interference)
Flooding occurs using a 3-way handshake :
  node A advertises newly available data using ADV (advertisement) message (containing dataʼ s meta-data)
  neighbor nodes (B, C, D, E) check if advertised data needed and if so, respond with REQ (request for data) message
  A sends DATA message to nodes that responded (i.e., B and D)

## Slide 279: SPIN-PP
Only nodes needed the advertised data respond
Nodes can aggregate received data with their own and advertise aggregate
Simple protocol
Nodes need to know their single-hop neighbors only
Lost ADV messages: periodically re-advertise
Lost REQ/DATA messages: re-request data of interest if data does not arrive within certain timeout interval
Protocol could also use explicit acknowledgments (e.g., REQ can contain list of data a node wants or does not want and using this list, a node can identify whether previous advertisements were received successfully)

## Slide 280: SPIN-EC and SPIN-BC
SPIN-EC:
  adds simple heuristic to protocol to add energy conservation
  as long as energy sufficient, node participates in 3-way handshake
  nodes does not participate if it believes that this will reduce its energy below a certain low-energy threshold
    node replies to ADV only if sufficient energy for transmitting REQ and receiving DATA
    node initiates handshake only if it has sufficient energy to send DATA to all neighbors
SPIN-BB:
  uses one-to-many communications (broadcast)
  receiver node waits for a random time interval before issuing REQ; if other node ʼ s REQ overheard, the receiver node cancels timer and does not send its own REQ
  advertiser broadcasts DATA only once (ignore duplicate REQs)

## Slide 281: SPIN-RL
Reliable version of SPIN-BC
  nodes keep track of overheard REQ messages
  if DATA message does not arrive within certain timeout interval, it assumes that either REQ or DATA did not arrive
  node broadcasts REQ to re-request data
    in message header, node specifies identity of randomly selected node among nodes that previously sent ADV for missing DATA
  SPIN-RL limits frequency with which DATA messages are sent
    once a node sends a DATA message, it will wait for certain amount of time before responding to other requests for the same data

## Slide 282: Directed Diffusion
Data-centric and application-aware dissemination protocol
Nodes request data by sending interests for named data
  data is named by attribute-value pairs
Interest dissemination sets up gradients within network to direct sensor data toward recipient
Intermediate nodes along the paths can combine data from different sources
  eliminates redundancy
  reduce number of transmissions

## Slide 283: Directed Diffusion: Attribute-Value Pairs
Simple vehicle-tracking application
  type = vehicle // detect vehicle location
  interval = 20 ms // send data every 20 ms
  duration = 10 s // perform task for 10 s
  rect = [-100,-100,200,200] // from sensors within rectangle

## Slide 284: Directed Diffusion
Interested node (sink) periodically sends interest to neighbors, which re-broadcast these messages (a)
Each node establishes a gradient towards the sink, which is a reply link toward the neighbor from which the interest was received (b)
Source can send data towards sink using these gradients (c)

## Slide 285: Directed Diffusion
Reinforcement:
  multiple paths from source to sink may exist
  sink can reinforce one particular neighbor based on some data-driven local rule
    example: sink could reinforce neighbor from which it has received a previously unseen event
    sink resends original interest message to that neighbor, which in turn reinforces one or more of its neighbors based on its own local rule
Comparison to SPIN:
  interests (queries) are issued on demand by the sink (instead of source advertisements)
    query-based approach may not be best solutions for networks with need for continuous data transfers (e.g., environmental monitoring)
  communication is all neighbor-to-neighbor (removing the need for addressing schemes and allowing nodes to perform aggregation and caching)

## Slide 286: Rumor Routing
Attempt to combine characteristics of event flooding (classic flooding) and query flooding (directed diffusion)
Nodes maintain two data structures:
  list of neighbors
  event table that contains forwarding information to all known events
    once an event is witnessed, it is added to the table (including a distance of 0) and an agent is generated with certain probability
    agent is a long-lived packet traveling the network to propagate information about this new event (and other events encountered along its route)
    once agent arrives at a node, the node can update its table

## Slide 287: Rumor Routing: Example
Node E reports new event E1 using agent
A receives agent via G and updates its table reflecting shorter distance to E1 via G

## Slide 288: Rumor Routing: Queries
When node wants to issue query for certain event:
  check if route towards event is in table
    if yes, forward query to next-hop neighbor indicated in table
    if no, pass query to randomly selected neighbor
  process is continued on each forwarding node and query collects list of recently seen nodes (to avoid revisiting them)
  TTL (time-to-live) counter is used to limit traveled distance
  if no response received after certain timeout value (i.e., the query did not reach the target), a different technique (classic flooding of the query) can be used

## Slide 289: Rumor Routing: Queries
Summary: strikes balance between query and event flooding
  query flooding may be too expensive with large query/event ratio
  event flooding may be too expensive when number of events large
  rumor routing propagates queries directly to nodes that seen event of interest
  latency secondary concern in rumor routing
  table can grow large with large number of events

## Slide 290: Gradient-Based Routing (GBR)
  Another variant of directed diffusion
  Gradient is determined on the basis of the number of hops to the sink
    a sink floods interest message
    each interest message records number of hops traveled
    therefore, a node can determine its distance (called height ) to sink
    gradient is difference between a node ʼ s height and height of neighbor
    packet is forwarded on the link with the largest gradient

## Slide 291: Gradient-Based Routing (GBR)
  Nodes can establish a Data Combining Entity (DCE), which is responsible for data compaction
  Nodes can use a traffic spreading technique to balance traffic over network
    stochastic scheme: node selects next hop randomly when there are two or more with same gradient
    energy-based scheme: node increases its height when its energy level is low
    stream-based scheme: new streams are diverted away from nodes that already serve other streams (e.g., by reporting increased heights)

## Slide 292: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 293: Proactive Routing
Routes are established before they are actually needed
Also called table-driven routing
Main advantage: routes can be used immediately when needed (table look up for next-hop neighbor)
Main disadvantages:
  establishing and maintaining routes that are infrequently (or never) needed
  routing tables can become very large
  stale information in tables can lead to routing errors

## Slide 294: Destination-Sequenced Distance Vector
DSDV is a modified version of class Distributed Bellman-Ford algorithm
Concept of distance-vector algorithms :
  node i maintains a list of distances {dijx} for each destination x via node j
  node i selects k as next-hop if dikx = min {dijx}
  distances stored in routing table , along with sequence number for each entry (assigned by destination node)
    purpose of sequence number is to identify stale routes
  nodes broadcast their routing tables to their neighbors periodically and whenever significant information is available
    full dump packet: contains entire routing table
    incremental packet: contains only changed table entries
    a receiving node updates its table if the received information has a more recent sequence number or if sequence number is identical, but new route is shorter

## Slide 295: DSDV: Example

## Slide 296: Optimized Link State Routing
OLSR is a protocol based on the link state algorithm
  nodes periodically broadcast topological information updates to all other nodes in the network
  allows nodes to obtain complete topological map and to compute paths
Nodes use neighbor sensing using HELLO messages:
  allows nodes to identify neighbors and to detect changes in neighborhood
  HELLO message contains nodeʼ s identity (address) and list of all known neighbors
  if node A can receive node B ʼs HELLO messages, but is not in node Bʼ s list of known neighbors, the link B A is asymmetric (otherwise symmetric )
  instead of flooding HELLO messages to all nodes in network, OLSR uses multipoint relays (MPRs)

## Slide 297: Optimized Link State Routing
    example: node determines its 2-hop neighbors (using HELLO messages) and selects minimum set of 1-hop neighbors to reach all 2-hop neighbors
  only MPRs forward messages to other nodes
  HELLO messages contain addresses of MPRs, i.e., a node advertises its reachability via MPRs only instead of all neighbors
Multipoint relays:
  a node selects a set of symmetric neighbors as MPRs (MPR selector set); each node can use different algorithm/heuristic for the selection process

## Slide 298: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 299: On-Demand (Reactive) Routing
Routes are not established until actually needed
Instead, a source node (knowing the identity/address of a destination node) initiates a route discovery process which completes when at least one route has been found or all possible paths have been examined
A newly discovered route is then maintained until it either breaks or is no longer needed by the source

## Slide 300: Ad Hoc On-Demand Distance Vector
AODV relies on broadcast route discovery mechanism, which is used to dynamically establish route table entries at intermediate nodes
Path discovery process:
  initiated whenever a source needs to transmit data to a sink and the source does not have an entry for the sink in its routing table
  source broadcasts route request (RREQ) packet containing:
    addresses of source and sink
    hop count value
    broadcast ID (incremented whenever source issues a new RREQ)
    two sequence numbers
  upon receiving RREQ, if a node knows a route to the destination, responds by sending a unicast route reply (RREP) message back to source
  otherwise RREQs are re-broadcast or duplicate RREQs (identified by source address and broadcast ID) are discarded

## Slide 301: Ad Hoc On-Demand Distance Vector
Use of sequence numbers:
  every node maintains own sequence numbers
  sourceʼ s RREQ includes its own sequence number and the most recent sequence number (if known) from the destination
  intermediate nodes only reply to RREQ if the sequence number of their route to the destination is greater than or equal to the destination sequence number in the RREQ
  when RREQ is re-broadcast, node records the address of neighbor from which RREQ came (establishing a reverse path towards source)
  as RREP travels towards source, intermediate nodes set up forward pointers to the node from which the RREP came and records latest destination sequence number

## Slide 302: Ad Hoc On-Demand Distance Vector
Use of RREPs:
  RREP contains:
    addresses of source and destination
    destination sequence number
    hop count
  intermediate node propagates RREP only if
    this is the first copy of this RREP the node sees
    or destination sequence number in RREP is greater than that of previous RREP
    or destination sequence number is the same as in previous RREP, but the hop count is smaller
  limits the number of RREPs in network and ensures that the RREP over the shortest route reaches the source

## Slide 303: Ad Hoc On-Demand Distance Vector

## Slide 304: Ad Hoc On-Demand Distance Vector
Routes expire after certain amount of time
Link state monitored using HELLO messages among neighbors
  when a link/route breaks, the node noticing this issues a route error (RRER) packet towards the source (which can re-initiate route discovery)
Summary:
  routes are established only when needed
  no need for route table updates and exchanges for unused routes
  periodic HELLO messages
  initial transmission delay if route must be discovered first
  RREP uses reverse path of RREQ, i.e., AODV assumes symmetric links

## Slide 305: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 306: Hierarchical Routing
Cluster head:
  responsible for propagating sensor data to sink
  sometimes more powerful than “regular” nodes
  experiences more traffic than “regular” nodes
Challenges in cluster formation:
  selection (election) of cluster heads
  selection of cluster to join
  adaptation of clusters in response to topology changes, failures, etc.
Advantages:
  potentially fewer collisions (compared to flat routing)
  easier duty cycling (energy efficiency)
  easier routing process (though routes may be longer)
  easier in-network data aggregation

## Slide 307: Variations of Hierarchical Routing

## Slide 308: Landmark Routing
Landmark: node to which its neighbors within certain number of hops know a route to that node
Example:
  nodes 2…6 have routes to node 1
  node 1 is a landmark “visible” to all nodes within 2-hop distance, i.e., node 1 is a landmark of radius 2
Node i for which nodes within n hops have routes toward is a landmark of radius n

## Slide 309: Landmark Routing
Hierarchy of landmarks: packet can be forwarded toward a destination by choosing an appropriate sequence of landmarks
Example:
  landmark address of node LM0: LM2.LM1.LM0
  source has entry for LM2: packet travels towards LM2
  once packet reaches node within range of LM1: packet travels towards LM1
  once packet reaches node within range of LM0: packet travels to LM0

## Slide 310: LEACH
Low-Energy Adaptive Clustering Hierarchy
Combines clustering with MAC-layer techniques (see previous discussion on LEACH MAC layer)
Assumes that cluster heads can communicate directly with base station
Cluster heads are responsible for forwarding sensor data to base station
Cluster heads are responsible for data aggregation to eliminate redundancy

## Slide 311: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 312: Location-Based Routing
Also referred to as geographic routing
Used when nodes are able to determine their (approximate) positions
Nodes use location information to make routing decisions
  sender must know the locations of itself, the destination, and its neighbors
  location information can be queried or obtained from a location broker
Types of geographic routing:
  unicast: single destination
  multicast: multiple destinations
  geocast: data is propagated to nodes within certain geographic area

## Slide 313: Unicast Location-Based Routing
One single destination
Each forwarding node makes localized decision based on the location of the destination and the node ʼ s neighbors ( greedy forwarding)
Challenge: packet may arrive at a node without neighbors that could bring packet closer to the destination (voids or holes)

## Slide 314: Greedy Perimeter Stateless Routing
In GPRS, a node forwards packet to neighbor that is geographically closest to the destination
Challenge of voids/holes (example: x is closer to the destination its neighbors w and y)
GPRS uses right-hand rule to traverse graph
  when a packet arrives at node x from node y, the next edge traversed is the next one sequentially counterclockwise (反时针方向) about x from edge (x,y)
  right-hand rule traverses interior of a polygon in clockwise edge order and exterior region in counterclockwise edge order

## Slide 315: Greedy Perimeter Stateless Routing
Sequence of edges traversed according to rule is called perimeter
In non-planar graphs, right-hand rule may take tour of edges that does not trace the boundary of a closed polygon
To obtain planar graphs, crossing edges must be removed (without partitioning the network)
  Relative Neighborhood Graph (RNG)
  Gabriel Graph (GG)
Example: RNG
  lune between u and v (intersection of radio ranges) must be empty of any witness node w such that edge (u,v) can be included in the RNG (i.e., if this region is nonempty, the link (u,v) will be removed)

## Slide 316: Forwarding Strategies
Greedy: minimize distance to destination in each hop
Nearest with Forwarding Progress (NFP): nearest of all neighbors that make positive progress (in terms of geographic distance) toward destination
Most Forwarding Progress within Radius (MFR): neighbor that makes greatest positive progress (progress is distance between source and its neighbor node projected onto a line drawn from source to destination)
Compass Routing: neighbor with smallest angle between a line drawn from source to the neighbor and the line connecting source and destination

## Slide 317: Geographic Adaptive Fidelity
GAF was primarily designed for networks with mobile nodes
Network region is divided into virtual grid
In each cell, only one node is a forwarder at any given time (all other nodes can sleep)
Assumption: all nodes within a cell can communicate with all nodes within all adjacent cells

## Slide 318: Geographic Adaptive Fidelity
Discovery state:
  nodes are initially in the discovery state, listen for messages from other nodes within cell
  when timer expires, node broadcasts discovery message and enters active state
Active state:
  node periodically re-broadcasts discovery messages
  node sets another timer to re-enter discovery state after timer expiration
Sleep state:
  entered whenever node determines that some other node is forwarder
  nodes periodically re-enter discovery state
Forwarder node:
  determined using negotiation process
  nodes in active state win over nodes in discovery state
  node IDs used to break ties

## Slide 319: Multicast Location-Based Routing
Multicast: deliver the same packet to multiple receivers
Simple solution 1: deliver copies of same packet to each individual receiver via unicast routing
  resource-inefficient
Simple solution 2: flood the entire network
  resource-inefficient
Concerned with efficiently delivering the same packet to receivers, i.e., minimize the number of links the packet has to travel
Common approach: multicast tree rooted at source and destinations are leaf

## Slide 320: Geocasting
Packet is sent to all or some nodes within specific geographic region
Example: query sent to all sensors within geographic area of interest
Routing challenge:
  propagate a packet near the target region (similar to unicast routing)
  distribute packet within the target region (similar to multicast routing)

## Slide 321: Roadmap
Routing basics
Data-centric routing
Proactive routing
On-demand routing
Hierarchical routing
Location-based routing
QoS-based routing

## Slide 322: QoS-Based Routing Protocols
Protocols that explicitly address one or more Quality-of-Service (QoS) metrics
Examples of QoS metrics:
  low (end-to-end) latency/delay
  low jitter
  low energy consumption
  low bandwidth requirements
  high reliability

## Slide 323: SPEED
Support for soft real-time applications, providing real-time unicast, real-time area-multicast, real-time area-anycast
Location-based routing
Periodic HELLO (beacon) messages
  node ID
  position
  average receive delay
Each node maintains neighbor table with the following entries for each neighbor:
  node ID
  position
  expiration time (ExpireTime)
  ReceiveFromDelay
  SendToDelay (delay received from beacon message)
ReceiveFromDelay values of all neighbors are averaged periodically to obtain single receive delay

## Slide 324: SPEED
Routing component: Stateless Nondeterministic Geographic Forwarding (SGNF)
Neighbor set of i : neighbors of i at least distance K away from i
Forwarding candidate set FSiDest: all neighbors that are at least distance K closer to destination
  neighbor j is in set if L-Lnext≥ K
    L = d(i,dest)
    Lnext = d(j,dest)
Packets are forwarded to nodes in FSiDest only; if empty, packet is dropped
FSiDest further subdivided:
  set of nodes with SendToDelay less than certain single hop delay D
  set of all other nodes

## Slide 325: SPEED
Forwarding candidate is selected from first group where nodes with higher relay speed have a greater chance of being selected.
Relay speed considers both distance and delays:
If there are no nodes in the first set, a relay ratio can be calculated, based on SPEEDʼs neighborhood feedback loop
  responsible for determining relay ratio by looking at miss ratios of neighbors
  if relay ratio is less than randomly selected number between 0 and 1, packet is dropped
  goal is to keep system performance at desired value, attempting to keep single hop delay below D

## Slide 326: SPEED
Back-pressure rerouting protocol of SPEED is responsible for
  preventing voids that occur when nodes fail to find next hop node
  reducing congestion using a feedback approach

## Slide 327: Summary

## Slide 328: Chapter 7 Time Synchronization

## Slide 329: Roadmap
The time synchronization problem
Time synchronization in wireless sensor networks
Basic techniques for time synchronization
Time synchronization protocols

## Slide 330: Clocks and the Synchronization Problem
Common time scale among sensor nodes is important for a variety of reasons
  identify causal relationships between events in the physical world
  support the elimination of redundant data
  facilitate sensor network operation and protocols
Typical clocks consist of quartz-stabilized oscillator (石英震荡器) and a counter that is decremented with every oscillation of the quartz crystal

## Slide 331: Clocks and the Synchronization Problem
When counter reaches 0, it is reset to original value and interrupt is generated
Each interrupt (clock tick) increments software clock (another counter)
Software clock can be read by applications using API
Software clock provides local time with C(t) being the clock reading at real time t
Time resolution is the distance between two increments (ticks) of software clock

## Slide 332: Clock Parameters
Clock offset: difference between the local times of two nodes
Synchronization is required to adjust clock readings such that they match
Clock rate: frequency at which a clock progresses
Clock skew: difference in frequencies of two clocks
Clock rate dC/dt depends on temperature, humidity, supply voltage, age of quartz, etc., resulting in drift rate (dC/dt-1)

## Slide 333: Clock Parameters
Maximum drift rate ρ given by manufacturer (typical 1ppm to 100ppm)
Guarantees that:
Drift rate causes clocks to differ even after synchronization
Two synchronized identical clocks can drift from each other at rate of at most
To limit relative offset to δ seconds, the resynchronization interval must meet the requirement:

## Slide 334: Clock Parameters
C(t) must be piecewise continuous (strictly monotone function of time)
  clock adjustments should occur gradually, e.g., using a linear compensation function that changes the slope of the local time
  simply jumping forward/backward in time can have unintended consequences
    time-triggered events may be repeated or skipped

## Slide 335: Time Synchronization
External synchronization
  clocks are synchronized with external source of time (reference clock)
  reference clock is accurate real-time standard (e.g., UTC)
Internal synchronization
  clocks are synchronized with each other (no support of reference clock)
  goal is to obtain consistent view of time across all nodes in network
  network-wide time may differ from external real-time standards

## Slide 336: Time Synchronization
External synchronization also provides internal synchronization
Accuracy (准确度): maximum offset of a clock with respect to reference clock
Precision (精度): maximum offset between any two clocks
If two nodes synchronized externally with accuracy of Δ, also synchronized internally with precision 2Δ

## Slide 337: Why Time Synchronization in WSNs?
Sensors in WSNs monitor objects and events in the physical world
Accurate temporal correlation is crucial to answer questions such as
  how many moving objects have been detected?
  what is the direction of the moving object?
  what is the speed of the moving object?
If real-time ordering of events is <<, then sensor times should reflect this ordering: ()<()<()

## Slide 338: Why Time Synchronization in WSNs?
Time difference between sensor time stamps should correspond to real-time differences: Δ= () - ()= -
  important for data fusion (aggregation of data from multiple sensors)
Synchronization needed by variety of applications and algorithms
  communication protocols (at-most-once message delivery)
  security (limit use of keys, detect replay attacks)
  data consistency (caches, replicated data)
  concurrency control (atomicity and mutual exclusion)
  medium access control (accurate timing of channel access)
  duty cycling (know when to sleep or wake up)
  localization (based on techniques such as time-of-flight measurements)

## Slide 339: Challenges for Time Synchronization
Traditional protocols (e.g., NTP) are designed for wired networks
Environmental effects
  sensors often placed in harsh environments
  fluctuations in temperature, pressure, humidity
Energy constraints
  finite power sources (batteries)!
  time synchronization solutions should be energy-efficient
Wireless medium and mobility
  throughput variations, error rates, radio interferences, asymmetric links
  topology changes, density changes
  node failure (battery depletion)
Other challenges
  limited processor speeds or memory (lightweight algorithms)
  cost and size of synchronization hardware (GPS)

## Slide 340: Synchronization Messages
Pairwise synchronization: two nodes synchronize using at least one message
Network-wide synchronization: repeat pairwise synchronization throughout network
One-way message exchange:
  single message containing a time stamp
  difference can be obtained from (-)=D+δ(D=propagation delay)

## Slide 341: Synchronization Messages
Two-way message exchange:
  receiver node responds with message containing three time stamps
  assumption: propagation delay is identical in both directions and clock drift does not change between measurements

## Slide 342: Receiver-Receiver Synchronization
So far: sender-receiver approaches
Receiver-receiver: multiple receivers of broadcast messages exchange their message arrival times to compute offsets among them
Example: 2 receivers; 3 messages (1 broadcast, 2 exchange messages)
No time stamp in broadcast message required

## Slide 343: Nondeterminism of Communication Latency
Several components contribute to total communication latency
Send delay:
  generation of synchronization message
  passing message to network interface
  includes delays caused by OS, network protocol stack, device driver
Access delay:
  accessing the physical channel
  mostly determined by medium access control (MAC) protocol
Propagation delay:
  actual time for message to travel to sender (typically small)
Receive delay:
  receiving and processing the message
  notifying the host (e.g., interrupt)

## Slide 344: Nondeterminism of Communication Latency

## Slide 345: Reference Broadcasts
Global Positioning System (GPS) is a well-known global source of time
  time measured from epoch started at 0h January 6, 1980 UTC
  unlike UTC, GPS not perturbed by leap seconds
    GPS is ahead by 15 seconds (and increasing)
Terrestrial radio stations
  WWV/WWVH & WWVB (National Institute of Standards &Technology)
  continuously broadcast time based on atomic clocks
Problems with these techniques:
  not universally available (underwater, indoors, outer space)
  need for high-power receivers
  size
  cost

## Slide 346: Lightweight Tree-Based Synchronization
Goal of LTS is to provide specified precision with little overhead
Based on pairwise synchronization:
message from j to k, containing time stamp (jʼs clock)
message from k to j, containing (jʼs clock) and , (kʼs clock)
assuming message delay D

## Slide 347: Lightweight Tree-Based Synchronization
Centralized multi-hop version of LTS
  reference node is root of spanning tree containing all nodes
  breadth first search used to construct tree
  once tree established, reference nodes synchronizes with children
  errors from pairwise synchronization are additive
    keep depth of tree small
  overhead of pairwise synchronization: 3 messages
  overhead of network-wide synchronization: 3n-3 messages (n edges)

## Slide 348: Lightweight Tree-Based Synchronization
Distributed multi-hop version of LTS
  one or more reference nodes contacted by sensors whenever synchronization is required
  nodes determine resynchronization period based on desired clock accuracy, distance to reference node, clock drift ρ, time of last synchronization
  node can query neighbors for pending synchronization requests, i.e., node synchronizes with neighbor instead of reference node

## Slide 349: Timing-sync Protocol for Sensor Networks
TPSN is another sender-receiver technique
  Uses a tree to organize network
  Uses two phases for synchronization
    discovery phase
    synchronization phase

## Slide 350: Timing-sync Protocol for Sensor Networks
Level discovery phase
  establish hierarchical topology
  root initiates phase by broadcasting level_discovery message (contains level and identity of sender)
  receiver can determine own level (level of sender plus one)
  receiver re-broadcasts message with its own identity and level
  receiver discards multiple received broadcasts
  if node does not know its level (corrupted messages, etc.), it can issue level_request message to neighbors (which reply with their levels)
    nodeʼs level is then one greater than the smallest level received
    node failures can be handled similarly (i.e., if all neighbors at level i-1 disappear, node issues level_request message
    if root node dies, nodes in level 1 execute leader election algorithm

## Slide 351: Timing-sync Protocol for Sensor Networks
Synchronization phase
  pairwise synchronization along the edges of hierarchical structure
  each node on level i synchronizes with nodes on level i-1
    approach similar to LTS:
– node j issues synchronization pulse at (containing level and time stamp)
– node k receives message at and responds with an ACK at (containing , , , and level)
– node j receives ACK at
    node j calculates drift and propagation delay

## Slide 352: Timing-sync Protocol for Sensor Networks
Synchronization phase (contd.)
  phase initiate by root node issuing time_sync packet
  after waiting for random interval (to reduce contention), nodes in level 1 initiate two-way message exchange with root node
  nodes on level 2 will overhear synchronization pulse and initiate twoway message exchange with level 1 nodes after random delay
  process continues throughout network
Synchronization error of TPSN
  depth of hierarchical structure
  end-to-end latencies

## Slide 353: Flooding Time Synchronization Protocol
Goals of FTSP include:
  network-wide synchronization with errors in microsecond range
  scalability up to hundreds of nodes
  robustness to topology changes
FTSP uses single broadcast message to establish synchronization points
Decomposes end-to-end delay into different components

## Slide 354: Flooding Time Synchronization Protocol
: wireless radio informs CPU that it is ready for next message
: interrupt handling time (few microseconds)
: CPU generates time stamp
: encoding time (transform message into electromagnetic waves; deterministic, low hundreds of microseconds)
: propagation delay (from t3on node I to on node j; typically very small and deterministic)
: decoding time (deterministic, low hundreds of microseconds)
: byte alignment time (delay caused by different byte alignments (bit offsets), i.e., receiving radio has to determine the offset from a known synchronization byte and then shift incoming message accordingly); can reach several hundreds of microseconds
: interrupt, CPU obtains time stamp

## Slide 355: Flooding Time Synchronization Protocol
Time-stamping in FTSP
sender sends single broadcast containing time stamp (estimated global time)
receiver extracts time stamp from message and time-stamps arrival (leads to global-local time pair, providing a synchronization point)
synchronization message begins with preamble followed by SYNC bytes, data field, and CRC
preamble bytes are used to synchronize receiver radio to carrier frequency
SYNC bytes are used to calculate bit offset

## Slide 356: Flooding Time Synchronization Protocol
Time-stamping in FTSP (contd.)
  multiple time stamps are used at both sender and receiver to reduce jitter of interrupt handling and encoding/decoding times
  time stamps are recorded at each byte boundary after the SYNC bytes as they are transmitted or received
  time stamps are normalized by subtracting appropriate integer multiple of nominal byte transmission time (e.g., approx. 417μs on Mica2)
  jitter in interrupt handling can be reduced by taking the minimum of normalized time stamps
  jitter in encoding/decoding can be reduced by averaging these corrected normalized time stamps
  final (error-corrected) time stamp is added into data part of message
  at receiver side, time stamp must further be corrected by the byte alignment time (can be determined from transmission speed and bit offset)

## Slide 357: Flooding Time Synchronization Protocol
Multi-hop synchronization
  root node is elected based on unique node IDs
  root node maintains global time and all other nodes synchronize to root
  synchronization is triggered by broadcast message by the root node
    whenever node does not receive synchronization message for certain amount of time, it declares itself to be the new root
    whenever root receives a message from node with lower node ID, it gives up root status
  all receiver nodes within range establish synchronization points
  other nodes establish synchronization points from broadcasts of synchronized nodes that are closer to the root
  a new node joining the network with lowest node ID will first collect synchronization messages to adjust its own clock before claiming root status

## Slide 358: Chapter 8 Localization

## Slide 359: Roadmap
Ranging techniques
Range-based localization
Range-free localization
Event-driven localization

## Slide 360: Overview
Without knowledge of location of a sensor, the information produced by such sensor is of limited use
  location of sensed events in the physical world
  location-aware services
  location often primary sensor information (supply chain management, surveillance)
  object tracking
  protocols based on geographic information (routing)
  coverage area management
Location often not known a priori, therefore, localization is the task of determining the position (e.g., coordinates) of a sensor or the spatial relationships among objects

## Slide 361: Overview
Global position
  position within general global reference frame
  Global Positioning System or GPS (longitudes, latitudes)
  Universal Transverse Mercator (莫卡托方位法) or UTM (zones and latitude bands)
Relative position
  based on arbitrary coordinate systems and reference frames
  distances between sensors (no relationship to global coordinates)
Accuracy versus precision
  GPS: true within 10m for 90% of all measurements
    accuracy: 10m (“how close is the reading to the ground truth?”)
    precision: 90% (“how consistent are the readings?”)
Symbolic position information
  “office 354”
  “mile marker 17 on Highway 23”

## Slide 362: Ranging Techniques
Time of Arrival (ToA, time of flight)
  distance between sender and receiver of a signal can be determined using the measured signal propagation time and known signal velocity
  sound waves: 343m/s, i.e., approx. 30ms to travel 10m
  radio signals: 300km/s, i.e., approx. 30ns to travel 10m
One-way ToA
  one-way propagation of signal
  requires highly accurate synchronization of sender and receiver clocks
Two-way ToA
  round-trip time of signal is measured at sender device
  third message if receiver wants to know the distance

## Slide 363: Ranging Techniques
Time Difference of Arrival (TDoA)
  two signals with different velocities
  example: radio signal (sent at and received at ), followed by acoustic signal (sent at = + and received at )
  no clock synchronization required
  distance measurements can be very accurate
  need for additional hardware

## Slide 364: Ranging Techniques
Angle of Arrival (AoA)
  direction of signal propagation
  typically achieved using an array of antennas or microphones
  angle between signal and some reference is orientation
  spatial separation of antennas or microphones leads to differences in arrival times, amplitudes, and phases
  accuracy can be high (within a few degrees)
  adds significant hardware cost

## Slide 365: Ranging Techniques
Received Signal Strength (RSS)
  signal decays with distance
  many devices measure signal strength with received signal strength indicator (RSSI)
    vendor-specific interpretation and representation
    typical RSSI values are in range of 0..RSSI_Max
    common values for RSSI_Max: 100, 128, 256
  in free space, RSS degrades with square of distance
  expressed by Friis transmission equation
  in practice, the actual attenuation depends on multipath propagation effects, reflections, noise, etc.
  realistic models replace with (n=3..5)

## Slide 366: Triangulation
Example of range-based localization
Uses the geometric properties of triangles to estimate location
Relies on angle (bearing) measurements
Minimum of two bearing lines (and the locations of anchor nodes or the distance between them) are needed for two-dimensional space

## Slide 367: Triangulation
Unknown receiver location
Bearing measurements from N anchor points:
Known anchor locations
Actual (unknown) bearings
Relationship between actual and measured bearings is β=+δθ with δθ= being the Gaussian noise with zero-mean and NxN covariance matrix S=diag()
Relationship between bearings of N anchors and their locations:
Maximum likelihood (ML) estimator of receiver location is then:
This non-linear least squares minimization can be performed using Newton-Gauss iterations:

## Slide 368: Trilateration
Localization based on measured distances between a node and a number of anchor points with known locations
Basic concept: given the distance to an anchor, it is known that the node must be along the circumference of a circle centered at anchor and a radius equal to the node-anchor distance
In two-dimensional space, at least three non-collinear anchors are needed and in three-dimensional space, at least four non-coplanar anchors are needed

## Slide 369
n anchor nodes: =() (i=1..n)
Unknown sensor location x=(x,y)
Distances between sensor and anchors known (, i=1..n)
Relationships between anchor/sensor positions and distances (2 dimensions):
This can be represented as Ax=b with:

## Slide 370: Trilateration
Based on this least squares system, we can obtain estimation of position (x,y) using x=
Anchor positions and distance measurements are inaccurate, therefore, if they are based on Gaussian distributions, we can assign a weight to each equation i:
The least squares system is then again Ax=b with:
The covariance matrix of x is then

## Slide 371: GPS-Based Localization
Global Positioning System
  most widely publicized location-sensing system"
  provides lateration framework for determining geographic positions
  originally established as NAVSTAR (Navigation Satellite Timing and Ranging)
  only fully operational global navigation satellite system (GNSS)
  consists of at least 24 satellites orbiting at approx. 11,000 miles
  started in 1973, fully operational in 1995
Two levels of service:
  Standard Positioning Service (SPS)
    available to all users, no restrictions or direct charge
    high-quality receivers have accuracies of 3m and better horizontally
  Precise Positioning Service (PPS)
    used by US and Allied military users
    uses two signals to reduce transmission errors

## Slide 372: GPS-Based Localization
Satellites are uniformly distributed in six orbits (4 satellites per orbit)
Satellites circle earth twice a day at approx. 7000 miles/hour
At least 8 satellites can be seen simultaneously from almost anywhere
Each satellite broadcasts coded radio waves (pseudorandom code), containing
  identity of satellite
  location of satellite
  the satelliteʼs status
  data and time when signal was sent
Six monitor stations constantly receive satellite data and forward data to a master control station (MCS)
MCS is located near Colorado Springs, Colorado
MCS uses the data from monitor stations to compute corrections to the satellitesʼ orbital and clock information which are sent back to the satellites

## Slide 373: GPS-Based Localization
Satellites and receivers use accurate and synchronized clocks
Receiver compares generated code with received code to determine
  the actual code generation time of the satellite
  time difference Δ between code generation time and current time
  Δ expresses the travel time of the code from satellite to receiver

## Slide 374: GPS-Based Localization
Radio waves travel at the speed of light (approx. 186,000 miles/second)
With known Δ, the distance can be determined
Receiver knows that it is located somewhere on a sphere centered on the satellite with a radius equal to this distance
With three satellites, the location can be narrowed down to two points
  typically one of these two points can be eliminated easily
With four satellites, accurate localization is possible
  accurate positioning relies on accurate timing
  receiver clocks are much less accurate than atomic GPS clocks
  small timing errors lead to large position errors
    example: clock error of 1ms translates to a position error of 300km
  fourth sphere would ideally intersect with all three other spheres in one exact location
  spheres too large: reduce them by adjusting the clock (moving it forward)
  spheres too small: increase them by adjusting the clock (moving it backward)

## Slide 375: GPS-Based Localization
Most GPS receivers today can achieve good accuracy (e.g., 10m or less)
Additional advanced techniques can be used to further improve accuracy:
  example: Differential GPS (DGPS)
    relies on land-based receivers with exactly known locations
    they receive signals, compute correction factors, and broadcast them to GPS receivers
    GPS receivers correct their own measurements
GPS in wireless sensor networks
  prohibitive factors: power consumption, cost, size, need for LOS
  deployment can be limited to a few (more powerful) nodes
    used as anchor nodes and reference points for range-free localization techniques

## Slide 376: Ad Hoc Positioning System (APS)
Example of a range-free localization approach
  based on connectivity information instead of distance/angle measurements
  no additional hardware required (cost-effective)
APS is a distributed connectivity-based localization algorithm
  estimates node locations with the support of at least three anchor nodes
    localization errors can be reduced by increasing the number of anchors
  uses concept of DV (distance vector), where nodes exchange routing tables with their one-hop neighbors

## Slide 377: Ad Hoc Positioning System (APS)
Most basic scheme of APS: DV-hop
each node maintains a table {, , } (location of node i and distance in hops between this node and node i)
when an anchor obtains distances to other anchors, it determines the average hop length (“correction factor” ), which is then propagated throughout the network
given the correction factor and the anchor locations, a node can perform trilateration

## Slide 378: Ad Hoc Positioning System (APS)
Example with three anchors
  knows its distance to (50m) and (110m)
  knows its hop distance to (2) and (6)
  correction factor: (50+110)/(2+6) = 20 (estimated distance of a hop)
  corrections are propagated using controlled flooding, i.e., a node only uses one correction factor and ignores subsequently received ones

## Slide 379: Ad Hoc Positioning System (APS)
Variation of this approach: DV-distance method
  distances are determined using radio signal strength measurement"
  distances are propagated to other nodes
  provides finer granularity (not all hops are estimated to be the same size)
  more sensitive to measurement errors
Another variation: Euclidean method
  true Euclidian distances to anchors are used
  node must have at least two neighbors that have distance measurements to anchors and the distance between the two neighbors is known
  simple trigonometric relationships are used to determine the distance between node and anchor

## Slide 380: Lighthouse Approach
Example of an event-driven localization approach
Requirement: base station with light emitter
Idealistic light source: emitted beam of light is parallel (constant width b)
Light source rotates s. t. sensor sees beam of light for

## Slide 381: Lighthouse Approach
Perfectly parallel light beams are hard to realize in practice
Small beam spreads can result in large localization errors
  if b=10cm and spread=1°, b’=18.7cm at 5m distance
Beam width should be large to keep inaccuracies small
Solution: two laser beams that outline a “virtual” parallel beam
  only edges of the virtual beam are of interest